## Slide 1: Radiographic Positioning
MeRT2122
(10 ECTS)
Hailegebriel Shiferaw (MRT, PH, MSc)
Department of Medical Radiology Technology
Hawassa University
3/9/2020

## Slide 2: Radiographic Positioning
UNIT FOUR
Vertebral Column
3/9/2020

## Slide 3: Objectives
At the end of these lesson the student will be able to;
Given diagrams, radiographs, or dry bones, names and describe the bones of vertebral column.
Differentiate between the curves of the vertebral column, to include primary curves, compensatory curves, lordosis, kyphosis and scoliosis.
State the criteria used to determine positioning accuracy on the radiographs of the vertebral column
Evaluate radiographs of the vertebral column in terms of positioning, centring, image quality, radiographic anatomy and pathology.
3/9/2020

## Slide 4: What is spine?
3/9/2020

## Slide 5: SPINE
3/9/2020

## Slide 6: Anatomy
The vertebral column commonly referred to as spine.
Located posteriorly on the midsagittal plane of the body and extends inferiorly from the base of the skull to the tailbone to constitute the longitudinal axis or backbone of the axial skeleton.
A group of 33 bones stake on each other to form column
.
3/9/2020

## Slide 7: Anatomy …cont’d
The sturdy column
Supports the head
Surrounds and protects the spinal cord
Transmits the weigh of trunk to the lower limbs
Serves as articulation for the ribs of bony thorax and
Allows for the attachment of many muscles of back.
3/9/2020

## Slide 8: Anatomy …cont’d
The vertebral column is divided in to regions according to location and structure of the vertebrae
    Seven cervical located in the neck
    Twelve thoracic vertebrae constitute the posterior thorax
    Five lumbar vertebrae are located posterior to abdomen and form the lower back
    The sacrum and coccyx, both are located in the pelvis.
3/9/2020

## Slide 9: Anatomy …cont’d
The sacrum is formed by the fusion of five sacral vertebra and the coccyx are formed by fusion of four coccygeal segments in adulthood.
3/9/2020

## Slide 10: Curvature of the vertebral column
The spine is not a straight, inflexible column of bone.
The majority of the vertebral column is curved at birth, with its concavity facing forward.
Additional curvature occurs as the child starts to lift his head and begins to walk.
3/9/2020

## Slide 11: Curvature of the vertebral column
The anterior concavity is maintained in the thoracic and sacro-coccigeal regions hence they are given the name primary curve.
The secondary curves develope on the lumbar and cervical regions which are convex anteriorly.
3/9/2020

## Slide 12: Curvature of the vertebral …cont’d
On occasion, the normal curves of the vertebral column may become distorted as the result of disease, traums or congenital.
Kyphosis (an exaggerated thoracic curvature and more convex)- individuals suffering from osteoporosis
Lordosis (the lumbar curvature becomes exaggerated and more concave)-individuals who carryindg excessively heavey weight in front of the body, being very obese, wearing shoes with very high heels.
Scoliosis (an abnormal lateral curvature of the spine)- scolio-means bent, crooked
3/9/2020

## Slide 13: Curvature of the Spine
3/9/2020

## Slide 14: Characteristics of typical vertebra
Each vertebra is an irregularly shaped bone composed of two main parts:
Body
Vertebral arch
Body /centrum/
  is anterior, weight-bearing portion of vertebra
  Cylindrical in shape with a slightly flattened posterior surface.
  Superior and inferior surface of the body are flat and rough
3/9/2020

## Slide 15: Characteristics of typical vertebra
Vertebral arch
  is the posterior ringlike portion of the vertebra
  Attaches to the body to enclose an opening known as vertebral foramen through this channel spinal cord passes.
  Completely surrounds and protects the spinal cord
  is formed by two pedicles and two laminae.
3/9/2020

## Slide 16: Typical vertebra
3/9/2020

## Slide 17: Typical vertebra
3/9/2020

## Slide 18: Patient preparation
A patient preparing for a radiographic examination of the cervical spine should be instructed to remove:
    Any earrings
    Necklaces
    Eye glasses
    Oral appliances
    Etc
It may be necessary for the patient to remove clothing above the waist and wear a patient gown.
3/9/2020

## Slide 19: Patient preparation …cont’d
For radiographic of the Thoracic spine, patients must remove all clothing and jewellery above the waist and dress in a patients gown that is open in the back.
Lumbar spine radiography requires removal of all clothing above and below waist to eliminate possibility of artifacts on the film.
3/9/2020

## Slide 20: Patient preparation …cont’d
Traumatic care
If an accident victim arrives in the radiology department on a stretcher, extreme care must be taken.
Any clothing that interferes with the procedure may have to be carefully removed or cut away.
3/9/2020

## Slide 21: Radiographic Positioning of the Vertebral Column
3/9/2020

## Slide 22: Cervical spine
Anteroposterior (AP) Cervical spine
Clinical indications
Pathology involving the mid and lower cervical spine (C3 to C7)
Demonstrates clay shoveler’s fracture /avulsion fracture of the spinous process/, compression fractures, and herniated nucleus pulposus (HNP) etc.
3/9/2020

## Slide 23: Cervical spine …cont’d
Technical consideration
Film size: 18x24cm/24x30cm lengthwise
Grid: required
Collimation: to the soft tissue of neck crosswise and to film lengthwise.
Shielding: apply gonadal shield
Minimum subject image distance 100cm
3/9/2020

## Slide 24: Cervical spine …cont’d
Patient positioning
Assist the patient to the supine position on the radiographic table or standing in front of an upright grid with the posterior aspect of the head and shoulder against the stand Bucky.
Centre the midsagittal plane of the patient to the midline of the table.
3/9/2020

## Slide 25: Cervical spine …cont’d
Part Positioning
Extend the patient’s head so that a line between the upper occlusal plane and the mastoid tips become perpendicular to the film plane.
Central Ray
Direct the central ray 15 to 200 cephalad to a point slightly inferior to the most prominent point of the thyroid cartilage.
Centre the cassette to the central ray
3/9/2020

## Slide 26: Cervical spine …cont’d
Image Evaluation
Soft tissue of the neck, lower five cervical vertebrae and upper two thoracic vertebrae should be included in the collimated area.
Bony trabeculae should be seen within vertebral bodies.
The fourth cervical body should be in the middle of the film.
The mastoid tips should be symmetrical.
The mandible should be superimposed over the base of the skull.
The intervertebral disk spaces should be clearly demonstrated.
3/9/2020

## Slide 27: AP Cervical spine …cont’d
Breathing instruction
Instruct the patient to stop breathing during the exposure.
3/9/2020

## Slide 28: Lateral C -spine
Clinical indications
Pathology involving the cervical spine and adjacent soft tissue structures, including spondylosis and osteoarthritis
Technical consideration
Film size: 18x24cm/24x30cm
Grid is required
65-75 kvp
Collimate to the soft tissue of the neck crosswise and to the film size lengthwise.
SID 150cm
3/9/2020

## Slide 29: Lateral C –spine …cont’d
Shielding
Gonadal shield should be applied on all patients, specially children and adults of reproductive age.
Patient Positioning
Assist the patient to lateral erect position in front of the upright grid device with the arms positioned comfortably at the sides, either lateral may be performed depending on department protocol.
3/9/2020

## Slide 30: Lateral C –spine …cont’d
Part Positioning
Centre the coronal plane passing through the external auditory meatus (EAM) to the midline of the upright grid device.
Adjust the entire patient’s body to a true lateral position, with the shoulder nearest the film firmly against the upright grid device.
Elevate the patient’s chin slightly to prevent superimposition of the mandible over the anterior arch of C1.
Depress the shoulder as much as possible and suspend small sandbags of equal weight from each wrist for immobilization.
3/9/2020

## Slide 31: Lateral C -spine…cont’d
Central ray
Direct the central ray perpendicular to C4, located at the level of the uppermost part of the thyroid cartilage.
Breathing Instructions
Instruct the patient to take in a breath, blow it out, then hold it during the exposure.
3/9/2020

## Slide 32: Lateral C -spine…cont’d
Imaging evaluation
Soft tissue structures of the neck and C1 through C7 should be included in the collimated area.
Bony trabeculae should be seen within the vertebral bodies and spinous process.
The fourth cervical body should be in the middle of the film.
The inter vertebral disk spaces and spines process of C2 through C7 should be clearly demonstrated.
The first two cervical vertebrae should be seen free of superimposition of the mandible.
The EAM, should be superimposed.
3/9/2020

## Slide 33: Lateral C –spine
3/9/2020

## Slide 34: Oblique C -spine
Clinical indications
Pathology involving the cervical spine and adjacent soft tissue structures, including stenosis involving the intervertebral foramen
Both right and left oblique projections should be taken for comparison purposes.
Anterior oblique positions /RAO, LAO/ are preferred because of reduced thyroid doses.
3/9/2020

## Slide 35: Oblique C –spine …cont’d
Technical consideration
Film size: 18x24cm/24x30cm
Grid or non grid
Exposure factor 65-75 kvp
SID 100cm
Collimate to the soft tissue of the neck crosswise and to the film size lengthwise.
Shielding
Gonadal shield should be applied on all patients, specially children and adults of reproductive age.
3/9/2020

## Slide 36: Oblique C –spine …cont’d
Patient Positioning
Assist the patient to the AP seated or standing position in front of the upright grid device.
Note: The RAO and LAO projections may be substituted for the LPO and RPO projections.
3/9/2020

## Slide 37: Oblique C –spine …cont’d
Part positioning
Rotate the entire body and head to form a 450 angle between the coronal plane and the film; the shoulder nearest the film should be firmly positioned against the upright grid device.
Centre the cervical spine to the midline of the upright grid device;
Elevate the patient’s chin slightly to minimize superimposition of the mandible over the spine; both obliques are obtained.
3/9/2020

## Slide 38: Oblique C –spine …cont’d
Central Ray
Direct the central ray 150 to 200 cephalad to a point slightly inferior to the level of the most prominent point of the thyroid cartilage and through the fourth cervical vertebra.
Breathing Instructions
Instruct the patient to stops breathing during the exposure.
3/9/2020

## Slide 39: Oblique C –spine …cont’d
Image Evaluation
Soft tissue structure of the neck , lower five cervical vertebrae, and upper two thoracic vertebrae should be included in the collimated area.
The fourth cervical body should be in the middle of the film.
The intervertebral foramina furthest from the film should be clearly demonstrated.
C1 should be demonstrated without superimposition of the occipital bone.
The intervertebral disk spaces should be clearly demonstrate
The mandible should not be superimposed over the cervical vertebrae.
3/9/2020

## Slide 40: RAO C –spine
3/9/2020

## Slide 41: Atlas and Axis (Open mouth-Odontoid)
Antero- posterior
Clinical indications
Pathology (particularly fractures) involving C1 and C2 and adjacent soft tissue structures
Demonstrates odontoid and Jefferson fractures (the fracture of anterior and posterior arches of C1).
Technical consideration
Film size- 18x24cm/24x30cm
Grid required
65-75kvp
Collimate to the area of interest
Minimum SID 100cm
3/9/2020

## Slide 42: Atlas and Axis …cont’d
Shielding
Gonad shielding should be used in all patients
Patient positioning
Assist the patient to the supine position on the radiographic table.
Centre the midsagittal plane of the patient to the midline of the table
Adjust the axis of the patient parallel with the long axis of the table
3/9/2020

## Slide 43: Atlas and Axis …cont’d
Part Positioning
Instruct the patient to open the mouth as wide as possible
Position the patient’s head so that a line between the lower margin of the upper incisors and the base of the skull (level of the mastoid tips) is perpendicular to the film plane.
Central Ray
Direct the central ray perpendicular to C1 through the open mouth.
Centre the cassette to the central ray.
Breathing instructions
Instruct the patient to maintain the wide open mouth and say “ah” during the exposure.
3/9/2020

## Slide 44: Atlas and Axis …cont’d
Image Evaluation
The entire atlas and axis should be included in the collimated area
Bony trabiculae should be seen within the lateral masses of C1, the dens, and the vertebral body of C2.
C1 should be in the middle of the film.
The lateral masses should be equal distances from the rami of the mandible
The lower edge of the upper incisors should be even with the base of the skull.
3/9/2020

## Slide 45: AP Open-mouth
3/9/2020

## Slide 46: Cervicothoracic spine
Lateral swimmers’ position
Clinical indications
Pathology involving the inferior cervical spine, superior thoracic spine, and adjacent soft tissue structures
Various fractures (including compression fractures) and subluxation
This is a good projection when C7 to T1 is not visualized on the lateral cervical spine
3/9/2020

## Slide 47: Cervicothoracic …cont’d
Lateral swimmers’ position
Technical consideration
Film size 24x30cm
Grid required
70-85 kvp
SID 150cm
Collimate to the soft tissue of the neck crosswise and to film size lengthwise
3/9/2020

## Slide 48: Cervicothoracic …cont’d
Shielding
Gonadal shielding should be used on all patients, especially children and adults of reproductive age.
Patient positioning
Assist the patient to lateral recumbent/standing position on the radiographic table.
3/9/2020

## Slide 49: Cervicothoracic …cont’d
Part Positioning
Centre the midaxillary plane to the middle of the table.
Adjust the entire patient’s body to a true lateral position
The arm nearest the film raised above the head and the shoulder moved slightly anteriorly
The forearm or sponge should be used to support the patient’s head
Keeping the spine parallel to the table top.
Adjust the head so it is in true lateral position.
3/9/2020

## Slide 50: Cervicothoracic …cont’d
Part Positioning
Depress the shoulder furthest from the film rotate it slightly posteriorly to prevent superimposition of the shoulders over the spine, the thoracic spine should remain lateral for this projection.
Place a sheet of leaded rubber on the table behind the patient to reduce the amount of scatter radiation reaching the film and improve radiographic quality.
3/9/2020

## Slide 51: Cervicothoracic …cont’d
Central ray
Direct the central ray 3 to 50 cauded through T1, located at the level of the vertebral prominence
Centre the cassette to the central ray.
Breathing instruction
Instruct the patient to take in a breath, blow it out, then hold it during the exposure.
3/9/2020

## Slide 52: Cervicothoracic …cont’d
Image evaluation
Soft tissue structure of the neck and C5 through T4 should be included in collimated area.
Bony trabeculae should be seen within the vertebral bodies and spinous processes.
The vertebral disk space of C5 through T4 should be clearly demonstrated.
The vertebral bodies should appear box like, no rotation should be evident.
The humeral head should be separated.
3/9/2020

## Slide 53: Lateral swimmers’
3/9/2020

## Slide 54: Thoracic spine
AP Thoracic Spine
Clinical indications
Compression fractures
Subluxation
Kyphosis
Technical Consideration
Film size: 30x40, 15x40
Grid required
SID 100cm
Collimate to the spine crosswise and to film size lengthwise
3/9/2020

## Slide 55: Thoracic spine …cont’d
Shielding
Gonad shielding should be used on all patients, especially children and adults of reproductive age
Patient Positioning
Assist the patient to the supine position on the radiographic table. With knees and hips flexed and support the leg.
Centre the midsagittal plane of the patient to the midline of the table, the head and shoulder should not be rotated.
The patient arm should rest comfortably on the radiographic table.
3/9/2020

## Slide 56: Thoracic spine …cont’d
Central Ray
Direct the central ray perpendicular to the film through T7 or 1 to 2 inches below sternal angle
Centre the cassette to the central ray
Breathing instruction
Instruct the patient either to take slow, shallow breath or take a breath in, blow it out and hold during exposure.
3/9/2020

## Slide 57: Thoracic spine …cont’d
Image Evaluation
The vertebral bodies of C7 through L1 should be included in the collimated area
Bony trabeculae should be seen within the vertebral bodies.
The seventh thoracic body should be in the middle of the film
The sterno-clavicular joints should be symmetrical
Spinous process should be seen at the midline of the vertebrae
The intervertebral disc space should be clearly demonstrated
3/9/2020

## Slide 58: AP Thoracic Spine
3/9/2020

## Slide 59: Thoracic spine …cont’d
Lateral thoracic spine
Technical Consideration
Film Size: 30x40cm
Grid required
Exposure factor 70-85kvp
SID 100cm
Collimate to the spine
Apply gonad shield
Patient Positioning
Assist the patient to the left lateral position on the radiographic table.
Flex the knees and hip for comfort and balance.
3/9/2020

## Slide 60: Thoracic spine …cont’d
Part Positioning
Centre the midaxillary plane to the midline of the table.
Adjust the long axis of the spine to lie parallel with the long axis of the table, the right leg should lie directly over the left leg.
Adjust the body so that the line through the shoulders and another through the hips are perpendicular to the film plane.
Place a sheet of leaded rubber on the table behind the patient to reduce the amount of scatter radiation reaching the film to improve the amount the quality of the radiograph.
3/9/2020

## Slide 61: Thoracic spine …cont’d
Central ray
Direct the central ray perpendicular to the film through T7.
Centre the cassette to the central ray.
Breathing instruction
Instruct the patient either to take slow, shallow breaths during the exposure.
3/9/2020

## Slide 62: Thoracic spine …cont’d
Image evaluation
The vertebral bodies of T3 through L1 should be well visualized within the collimated area.
The vertebral bodies should equally be penetrated.
The vertebral bodies should appear boxlike.
The intervertebral disc spaces and pedicles should be clearly demonstrated.
3/9/2020

## Slide 63: Lateral thoracic spine
3/9/2020

## Slide 64: PA Oblique Thoracic spine
Clinical indications
Pathology involving the zygapophyseal joints of the thoracic spine.
Both right and left oblique projections are taken for comparison
3/9/2020

## Slide 65: PA Oblique Thoracic spine
Technical consideration
Film Size : 30x40cm
Grid required
70-85 kvp
SID 100cm
Appropriate collimation
Shielding
Apply gonad shield
3/9/2020

## Slide 66: PA Oblique Thoracic …cont’d
Patient positioning
Assist the patient to the left lateral position for LAO and to the right lateral position for RAO projection either lying or erect.
Rotate the patient 200 toward the film to form a 70° angle between the coronal plane and film.
The right arm should be elevated with the hand supported on the top of the grid device.
3/9/2020

## Slide 67: PA Oblique Thoracic …cont’d
Patient positioning
The left arm should be positioned with the elbow flexed and the back of the hand resting on the hip.
Centre the thoracic spine at the midline of the upright grid device. The shoulder nearest the film should be positioned firmly against the upright grid device.
3/9/2020

## Slide 68: PA Oblique Thoracic …cont’d
Central Ray
Direct the central ray perpendicular to the film through T7
Centre the cassette to the central ray
Breathing technique
Allow the patient shallow breathing or tell the patient to take breath in, below it out and hold during exposure
3/9/2020

## Slide 69: PA Oblique Thoracic …cont’d
Image Evaluation
The vertebral bodies of C7 through L1 should be well visualised within the collimated area.
Bony trabeculae should be seen within the vertebral bodies
The 7th thoracic body should be in the middle of the film
The first through 12th vertebral bodies should be adequately penetrated
3/9/2020

## Slide 70: LAO RAO
3/9/2020

## Slide 71: RAO
3/9/2020

## Slide 72: Lumbar spine
AP Lumbar spine
Clinical indications
Pathology of the lumbar vertebrae, including fractures, scoliosis, and neoplastic processes
Prepare the patient
The patient should be instructed to be on a low residue diet and to take laxative drug (dulcolax, caster oil or Epsom salt) during 24 hours prior to the examination. In the case of emergency radiography no bowel preparation is possible.
3/9/2020

## Slide 73: Lumbar spine …cont’d
Technical consideration
Film size 24x30cm
Grid required
70-80kvp
SID 100cm
Apply proper collimation
Shielding
Apply gonad shield
Patient positioning
Assist the patient to the supine position on the radiographic table; tell the patient to flex his/her knees and hips for proper contact with the table then to the film. Support the legs on suitable support.
3/9/2020

## Slide 74: Lumbar spine …cont’d
Part positioning
Centre the midsagittal plane of the patient to the midline of the table
Position the patient’s hands comfortably on the upper chest or radiographic table.
Central ray
Direct the central ray perpendicular to the film through the L4- 5 interspace (at the level of the iliac crests approximately 3 to 5 cm above the crest).
Centre the cassette to the central ray.
3/9/2020

## Slide 75: Lumbar spine …cont’d
Breathing instruction
Instruct the patient to take a breath in below it out and hold it out during exposure.
Image evaluation
The vertebral bodies of T12 through S2 should be included in the collimated area.
The iliac crest should be symmetrical.
Spinous processes should be seen at the midline of the vertebrae and in the middle of the film.
The intervertebral disc spaces should be clearly demonstrated.
3/9/2020

## Slide 76: AP Lumbar spine
.
3/9/2020

## Slide 77: Lateral Lumbar spine
Clinical indications
Pathology of the lumbar vertebrae including fractures, spondylolisthesis, neoplastic processes, and osteoporosis.
Technical Considerations
Film size 24x30 cm
Gird required
80- 90 kVP
SID 100cm
Collimate to the spine crosswise and to film size lengthwise.
3/9/2020

## Slide 78: Lateral Lumbar spine
Shielding
Gonadal shielding should be used on male patients, especially children and adults of reproductive age
Patient positioning
Assist the patient to the lateral recumbent position on the radiographic table, the patient may flex the knees and hips for comfort and balance.
Note: This projection can also be obtained with the patient erect.
3/9/2020

## Slide 79: Lateral Lumbar spine …cont’d
Part Positioning
Centre the midaxillary plane to the midline of the table, position the arms at a right angle with the body
Adjust the long axis of the spine to lie parallel with the long axis of the table.
The right leg should be directly over the left leg, a small sandbag between the knees will help prevent rotation.
3/9/2020

## Slide 80: Lateral Lumbar spine …cont’d
Part Positioning
Position a firm pillow under the head and radiolucent supports under the waist and lower thoracic area so the spine is parallel with the tabletop.
Adjust the body so a line through the shoulders and another through the hips are perpendicular to the film plane looking down from above the patient or head of the table will help detect any patient rotation.
3/9/2020

## Slide 81: Lateral Lumbar spine …cont’d
Central Ray
Direct the central ray perpendicular to the area of the spinal fusion. Approximately 1 to 1.5 in. Above the iliac crest.
Centre the cassette to the central ray.
Breathing instruction
Instruct the patient to take a breath in, below it out and hold it out during the exposure.
3/9/2020

## Slide 82: Lateral Lumbar spine …cont’d
Image evaluation
The vertebral bodies of T12 through S2 should be included in the collimated area.
The third lumbar vertebral body should be in the middle of the film.
The through fifth lumbar bodies should be adequately penetrated
The vertebral bodies should appear box like
The intervertebral disk spaces and pedicles should be clearly demonstrated
3/9/2020

## Slide 83: Lateral Lumbar spine
3/9/2020

## Slide 84: Right or Left Posterior/Anterior Oblique
Clinical indications
This projection demonstrates pars interarticularis /spondylosis/ and the apophyseal joints on the side nearest the cassette.
Both sides are taken for comparison
Technical consideration
Gird required
Film size 24x30cm
70-80kvp
SID 100cm
Apply proper collimation
Shielding
Apply gonad shield outside region of interest
3/9/2020

## Slide 85: Right or Left Posterior …cont’d
Patient positioning
Assist the patient to the supine position on the radiographic table and is then rotated 45° to the right and left side in turn. The patient’s arms are raised with the hands resting on the pillow.
The hips and knees are flexed and the patient is supported with a 45° foam pad placed under the trunk on the raised side.
The cassette is centred at the lower coastal margin
3/9/2020

## Slide 86: Right or Left Posterior …cont’d
Central ray
Direct the central ray towards the mid clavicular line on the raised side at the level of the lower costal margin
Breathing Instructions
Instruct the patient to take a breath in, blow it out, and hold it out during the exposure
3/9/2020

## Slide 87: Right or Left Posterior …cont’d
Image Evaluation
The vertebral bodies of T12 through S2 should be included in the collimated area.
The third lumbar vertebral body should be in the middle of the film.
When the RPO and LPO projections are compared the iliac should be symmetrical.
The right (RPO) or left (LPO) zygapophyseal joints should be clearly demonstrated.
3/9/2020

## Slide 88: RPO LAO
3/9/2020

## Slide 89: RPO
3/9/2020

## Slide 90: Lumbosacral Junction
AP Axial lumbosacral junction
Clinical indications
Pathology of L5-S1 and the sacroiliac joints
Technical consideration
Film size 18x24cm
Grid is used.
SID 100cm
Collimate the area of interest
Shielding
Gonad shield should be applied on male patients.
3/9/2020

## Slide 91: Lumbosacral Junction …cont’d
Patient positioning
Assist the patient to the supine position on the radiographic table.
The patients leg should be extended
Part positioning
Centre the midsagittal plane of the patient to the Medline of the x-ray table
Position the patient’s arm comfortably on the radiograph
3/9/2020

## Slide 92: Lumbosacral Junction …cont’d
Patient positioning
Central ray
Direct the central ray 300 for male and 350 for female cephalad
Breathing instruction
Instruct the patient to take a breath in, below it out and hold it out during the exposure.
3/9/2020

## Slide 93: Lumbosacral Junction …cont’d
Image evaluation
The vertebral bodies of L5 through S1 should be included in the collimated area
Bony trabeculae should be seen within the vertebral bodies
The iliac crests should be symmetrical
3/9/2020

## Slide 94: AP Axial Lumbosacral Junction
3/9/2020

## Slide 95: Lumbosacral Junction …cont’d
Lateral lumbosacral
Clinical indications
Spondylolisthesis involving L4-L5 or L5-S1 and other L5-S1 pathologies
Technical consideration
Film size 24x30cm
Grid required
85-100kvp
Collimate to the area of interest
Patient Positioning
Assist the patient to the left lateral position on the radiographic table, the patient may flex the knee and hips for comfort.
3/9/2020

## Slide 96: Lumbosacral Junction …cont’d
Part positioning
Centre the body to the midline of the table.
Position the arms at a right angle to the body.
Adjust the long axis of the spine to lie parallel with the long axis of the table.
The right leg should be directly over the left leg, a small sand bag between the knees will help prevent rotation.
Position a firm pillow under the head and a radiolucent supports under the waist and lower thoracic area.
3/9/2020

## Slide 97: Lumbosacral Junction …cont’d
Centre - to L5-S1 junction
Centre the cassette to the central ray.
Breathing instruction
Instruct the patient to take a breath in, blow it out, and hold it out during the exposure.
3/9/2020

## Slide 98: Lumbosacral Junction …cont’d
Image evaluation
The vertebral bodies of L5 through S1 should be visualised within the collimated area.
Bony trabeculae should be seen within the vertebral body
The L5- S1 intervertebral disc space should be clearly demonstrated in the middle of the film. It should be well penetrated.
The vertebral body of the L5 should appear box like.
3/9/2020

## Slide 99: Lateral Lumbosacral Junction
3/9/2020

## Slide 100: Sacrum
Anteroposterior (AP)
Clinical indications
Pathology of the sacrum, including fracture.
Technical Consideration
Film size 24x30cm Lengthwise.
Grid required
65-75 kvp
SID 100cm
Collimate to the area of interest
Shielding
Gonad shield should be used on male patient
Preparation
The patient should take cleansing enema to avoid fecal material and empty the bladder prior to radiographic examination
3/9/2020

## Slide 101: Sacrum …cont’d
Patient Position
Assist the patient to the supine position on the radiographic table.
Part Positioning
Centre the midsagittal plane of the patient to the midline of the table.
Position the patient’s hands comfortably on the upper chest or radiographic table.
Central Ray
Direct the central ray 150 cephalad to a point 2in superior to the syphysis pubis.
Centre the cassette to the central ray.
3/9/2020

## Slide 102: Sacrum …cont’d
Breathing Instruction
Instruct the patient to take a breath in, blow it out, and hold it out during the exposure.
Image Evaluation
The L5-S1 intervertebral disc space and superior rami of the pubic bone should be included.
Bony trabeculae should be seen within the sacrum.
The sacrum should be demonstrated in the middle of the film.
3/9/2020

## Slide 103: AP Sacrum (axial)
3/9/2020

## Slide 104: Sacrum …cont’d
Lateral Sacrum
Technical consideration
Film Size 24x30cm lengthwise
Grid required
70-85 kvp
SID 100cm
Collimate to the area of interest
Shielding
Gonad shield should be used
Patient Positioning
Assist the patient to the left lateral position on the radiographic table, the patient may flex the knee and hips for comfort.
3/9/2020

## Slide 105: Lateral Sacral
3/9/2020

## Slide 106: Coccyx
Anteroposterior (AP)
Clinical indications
Pathology of the coccyx including fracture
Technical Consideration
Film size 24x30cm Lengthwise.
Grid required
65-75 kvp
Sid 100cm
Collimate to the area of interest
Shielding
Gonad shield should be used on male patient
3/9/2020

## Slide 107: Coccyx …cont’d
Preparation
The patient should take cleansing enema to avoid fecal material and empty the bladder prior to radiographic examination.
Patient Position
Assist the patient to the supine position on the radiographic table.
Part Positioning
Centre the midsagittal plane of the patient to the midline of the table
Position the patient’s hands comfortably on the upper chest or radiographic table.
3/9/2020

## Slide 108: Coccyx …cont’d
Patient Position
Central Ray
Direct the central ray 100 caudad to a point 2in superior to the symphysis pubis.
Centre the cassette to the central ray.
Breathing Instruction
Instruct the patient to take a breath in, blow it out, and hold it out during the exposure.
3/9/2020

## Slide 109: Coccyx …cont’d
Image Evaluation
The coccyx and distal one third of the sacrum should be included.
The coccyx should be clearly demonstrated in the middle of the film.
The coccyx should be adequately demonstrated.
The coccyx should be directly above the symphysis pubis.
3/9/2020

## Slide 110: AP Coccyx (axial)
3/9/2020

## Slide 111: Lateral Coccyx
Technical consideration
Film size 18x24cm
Grid required
SID 100cm
Exposure factor 75- 85kvp
Apply proper collimation
Shielding
Apply gonad shield for male patient
Patient positioning
Assist the patient to the left lateral position on the radiographic table. The patient may flex knees and hips for comfort and balance
3/9/2020

## Slide 112: Lateral Coccyx …cont’d
Part Positioning
Centre the body to the midline of the table.
Adjust the long axis of the spine to lie parallel with long axis of the table, the right leg should be directly superimposed over the left leg.
Position pillow under the head
Central ray
Direct the central ray perpendicular to the coccyx
Centre the cassette to the central ray
3/9/2020

## Slide 113: Lateral Coccyx …cont’d
Breathing instruction
Instruct the patient to take a breath in, blow it out, and hold it out during exposure.
Image evaluation
The coccyx and distal end of the sacrum should be well visualized.
The coccyx should be clearly demonstrated in the middle of the film
The coccyx should be adequately penetrated
3/9/2020

## Slide 114: Lateral Coccyx
3/9/2020

## Slide 115
Thank You !
3/9/2020