## Slide 1
CENTRIFUGES
W Wieking, Food Tec GmbH, Oelde, Germany
Copyright 2002, Elsevier Science Ltd. All Rights Reserved
Introduction
Apart from thermal and extraction methods of separation, mechanical methods are most widely used for the separation of liquid suspensions and sludges into their different components. The basic processes of mechanically treating liquids are sedimentation, decantation, centrifugation, straining, filtering and pressing. These processes can be classified according to the physical properties which they utilize and the forces arising from them.
Classification of Centrifuges
Any attempt systematically to classify the different centrifuges, including gas centrifuges, arrives at the following main definition of the physical forces occurring in the centrifuge: gas separation, demulsi- fication, sedimentation and filtration (Figure 1). Demulsification is the separation of a liquid mixture into two liquid phases with different densities, which also mutually emulsify. Classified here must be liquid- liquid extraction and two-phase separation. Sedi- mentation processes take place during decantation, but also in combination with separation (i.e. solid- liquid-liquid separation) and filtration (liquid-solid separation). Filtration includes the filtration process and basket and filter centrifuges. Here, a combination with sedimentation is also possible.
Selection Criteria for Centrifuges
Separators are centrifuges for liquid-liquid separa- tion, for liquid-liquid solid separation or for liquid- solid separation. They have tubular discs or angular chamber bowls. Separators operate continuously in terms of discharges of the liquid phase. In respect of the solid discharge, they work either discontinuously (i.e. discontinuous disc-type centrifuges, which must be stopped, so that the collected solids can be removed by hand), semi-continuously (self-discharging disc- type centrifuges or self-cleaning separators) or fully continuously (nozzle-type separators). Decanters usually have an unperforated bowl (with the excep- tion of the screen centrifuge decanters, which are decanters with an added basket bowl) that operates continuously (see Figure 2).
General Field of Application
Discontinuous separators are suitable for liquid- liquid extraction, separation of liquid mixes and clari- fication of liquids. In addition to this self-cleaning separators can be used for the concentration of slur- ries and for wet classifications. The fields of applica- tion of nozzle-type separators are similar. These also cover the field of liquid-solid extraction. The decanter has the widest range of applications and, for this reason, is one of the most important centrifuges. As a three-phase decanter, it separates liquid mixes while simultaneously concentrating the solids and, as an extraction decanter, it is used for continuous solid-liquid extraction. Basket and pusher centrifuges are dewatering centrifuges in which washing can be carried out. A knife centrifuge, like the decanter, has a wide range of applications and is superior to all
Caseins see Milk Proteins: Casein Nomenclature, Structure and Association Properties; Caseins, Micellar Structure; Caseins, Functional Properties and Food Uses; Caseins, Industrial Production and Compositional Standards.
244 CENTRIFUGES

## Slide 2
other centrifuges, particularly in respect to the attainable dry solids content.
The selection criteria for the particular separation duty are of course dependent on the difference in specific weight when considering a liquid-liquid separation. One criterion for the solid part is particle size. Another important factor is the quantity of solids in the suspension. In Figure 3, separators, decanters, basket and filter centrifuges are listed in accordance with the size of suspended particles. In Figure 4, the criteria for selection based on solids content in the feed stock are illustrated. It is again
shown that separators are liquid-orientated, while decanter, basket, knife and pusher centrifuges are more suitable for solids.
Applications of Centrifuges in the Dairy Industry
Skimming
The dairy industry introduced centrifugal separation technology in the late nineteenth century. Starting from hand-driven machines, the development of
Separation
Gas centrifuge
G/G
Thin-layer centrifuge
Annular chamber extractor
Tube-type separator
Disc-type nozzle separator
Three-phase tube-type separator
Hydro- cyclone
Cup centrifuge (laboratory)
Disc-type nozzle centrifuge
Self- cleaning disc-type centrifuge
Annular chamber centrifuge
Tube-type centrifuge
Decanter
Screen centrifuge decanter
L/G
Gas separation
L/L
L/L
Demulsification
S/L/L
S/L
S/L
Sedimentation
Tumbler centrifuge
Basket screw centrifuge
S/L
Free- swinging centrifuge
Three-column centrifuge
Suspension pendulum centrifuge
Knife centrifuge (vertical)
Pusher centrifuge (single stage or multistage)
S/L
Filtration
Figure 1 Systematic classiication of centrifuges. G, gas; L, liquid; S, solid.
CENTRIFUGES 245
Isotope |  | Degasing |  | Extraction |  | Two-phase |  | Three-phase |  | Decantation |  | Combination | Basket |  | Filter
separation |  |  |  |  |  | separation |  | separation |  |  |  | sedimentation | centrifuge |  | centrifuge
 |  |  |  |  |  |  |  |  |  |  |  | filtration |  |  | 
Disc bowl |  | Self- |  | Double- |  | Baffle-ring |  | Oscillating |  | Siphon
extractor |  | cleaning |  | cone |  | centrifuge |  | screen |  | knife
 |  | separator |  | centrifuge |  |  |  | centrifuge |  | centrifuge
Spiral |  | Disc-type |  | Disc-type |  | Overflow |  | Differential |  | Slide |  | Knife
chamber |  | separator |  | separator |  | centrifuge |  | cone |  | centrifuge |  | centrifuge
extractor |  |  |  |  |  |  |  | decanter |  |  |  | 

## Slide 3
Liquid– liquid extraction
Separation of liquid mixtures
Clarifi- cation of liquids
Concen- tration of slurries
Solid– liquid extraction
Dehydration Dewatering
of amorphous substances
of crystalline Wet
substances classification
Discontinuous separators
Separators with self-cleaning bowl
Nozzle-type separators
Decanters
Basket centrifuges
Pusher-type centrifuges
Knife-type centrifuges
Figure 2
Functions of centrifuges according to technological applications.
Particle size in µm
Separator with clarifier bowl
Separator with self-cleaning bowl
Separator with nozzle bowl Decanter
Basket centrifuge Knife centrifuge Pusher centrifuge
1000
10 000 100 000
0.1
10
1
100
Figure 3
Separating ability of centrifuges according to the size of suspended particles.
Solids, % by volume
Separator with clarifier bowl
Separator with self-cleaning bowl Separator with nozzle bowl Decanter
Basket centrifuge Knife centrifuge Pusher centrifuge
70 80
90 100
10 20 30 40 50 60
0
Figure 4
Selection of type of centrifuge based on the solids content of the feedstock.
246 CENTRIFUGES

## Slide 4
electrical drives and the overall efficiency and capacity was the main focus for decades. At the end of the 1970s automatic discharging separators were introduced into the dairy industry with the capability of operating much longer, without stopping for cleaning. Today, skimming centrifuges can handle throughputs of up to 60 000 l h-1 on a single machine. The applications for skimming centrifuges in the dairy industry are the separation of:
warm milk
cold milk
whey
buttermilk
butteroil
retentates.
Fat constitutes about 30% of total milk solids. For the separation of fat from milk, the following criteria of milk variables are of great importance:
Nutritive value: breed of cow, lactation time, climate and feeding.
Physical properties: mechanical and heat treat- ment.
Chemical properties: enzyme reaction, bacterial influences.
The above-mentioned factors vary from country to country and must be considered on a local basis for the effective separation of milk. However, the effect of separation efficiency depends mainly on the fat globule size distribution in the whole milk, which is influenced by the factors stated in point 1 above. Having covered the effects during the production of the milk within the udder of the cow, the biggest effects on the quality of the milk occurs during the process of milking and the transporting, storage and treatment of the milk prior to separation. Mechanical treatments, such as pumping, cooling, agitating, heating and the introduction of air, influence separa- tion efficiency by damaging the fat globules.
Long cooling periods of, e.g. over 2-3 days, change the chemical properties of the fat globules because of the absorption of more water, which increases their density. This influences the skimming ability.
Separator design If the separation of fat globules from its carrier liquid (skim milk) in the separator bowl is considered as a physical process, then the sedimentation speed between the discs is subject to Stokes's law:
vz = 18
x
d2 x D.p
rJ x g x (
where vz = setting speed in centrifugal field (m s-1);
d = diameter of fat globule (m); D.p = p1 - p2;
p1 = density of fat globule (kg m-3); p2 = density of
skim milk (kg m-3); rJ = dynamic viscosity (kg m s-1);
g = acceleration due to gravity (9.81 m s-2); ( =
centrifugation coefficient I( = (r x w )/gl; r = radius
2
(m); w = angular velocity [1/S].
As the equation shows, the speed of sedimentation depends on the following factors:
difference in density between the particles to be separated (e.g. fat globules)
particle size
viscosity of the liquid
bowl speed
bowl radius
settling area of the discs.
As the density and dynamic viscosity are functions of the temperature, warm milk separation is always more efficient than cold milk separation. The optimum temperature for the separation of milk is about 55 oC. At temperatures above 60 oC, there is some precipitation of proteins, which have a negative effect on separation efficiency. These proteins form a thin film on the surface of the discs, and with disc interspaces of only 0.3-0.6 mm, these deposits have a detrimental effect on the conditions of flow (Figure 5).
A fat globule is considered to have been removed from the liquid when it reaches the upper surface of the disc below. Due to the negative value for D.p in Stokes's equation for the sedimentation speed, the fat globules move inwards against the centrifugal field in the disc interspace towards the centre of the separator bowl (Figure 6). Because fat globules are not pure fat (they are covered with a fat globule membrane which contains protein), fat globules smaller than 1 µm cannot be separated by centrifugal force because their
Sediment
Skim
Cream
Feed
r
r
Figure 5 Theoretical path of particle movement between two discs.
CENTRIFUGES 247

## Slide 5
specific weight is not sufficiently different from that of the carrier liquid.
A reduction in temperature from the optimum re- duces the separation efficiency due to the increase in viscosity until, at about 20-25 oC, a blockage of the cream flow occurs. Therefore, cold-milk separators differ from warm-milk separators in two main respects; they have:
a larger disc interspace
an open or hermetic cream discharge.
Cold-milk separators usually operate at a temper- ature between 4 and 12 oC and, as a general rule, any long-term mechanical treatment of milk should be avoided at a temperature between 15 and 50 oC because increased lipase activity will result as an in- creased level of free fatty acids.
Standardization
The direct automatic standardization systems are designed for on-line standardization of the fat content for standardized milk and cream. These systems usually have two control loops: one for the cream fat content and one for the standardized milk fat content. The fat content of the cream is obtained by adjusting its throughput via signals from the mass flow meter installed in the cream line. The fat content of the
standardized milk is obtained by dosing part of the cream to the skimmed milk.
Two flow transmitters and one mass flow meter are available for measuring the throughputs of:
cream from the centrifuge
cream to be incorporated
raw milk.
With this information, the computer can calculate the throughputs of other systems, namely:
standardized milk from the centrifuge
skim milk from the centrifuge
surplus standardized cream.
The mass flow meter measures the cream density and quantity. The computer transforms this density into fat content. Combining the information for fat content and throughput data, the computer regulates the system control valves for:
achieving the fat content required for the stand- ardized cream
reincorporating the necessary amount of stand- ardized cream in the skim milk, in order to obtain the required fat content of the standardized milk.
Clarification
In order to meet the requirements of national and international regulations, as well as customer ex- pectations, milk and milk products should undergo adequate clarification. Raw milk contains undesired constituents such as particles of dirt and blood, somatic cells and, of course, bacteria.
The clarification of milk can take place at a cold or warm temperature (3-12 oC or 52-58 oC). A tem- perature in the range 15-50 oC should not be used because fat damage occurs due to mechanical strain and the activity of enzymes. In respect to clarification efficiency of non-milk solids, temperature has very little influence. However, if bacteria are to be removed at the same time, only warm-milk clari- fication is efficient. Clarification of whey prior to fat separation is more and more common in large whey treatment plants; it results in better skimming of the whey and also in improved quality of the skimmed whey and whey cream due to a reduced level of fines in these products. The advantage of proper clari- fication also applies to other dairy products.
Separation of Whey
The separation of whey is a process that has been performed for decades. Today, in order to meet
1
2
3
4
5
6
7
9
8
Figure 6 Cross-section of bowl of a cream concentrator. 1, Feed; 2, cream discharge; 3, skim milk discharge; 4, skim milk pump; 5, cream pump; 6, discs; 7, soft stream inlet; 8, sediment- holding space; 9, sediment ejection ports.
248 CENTRIFUGES

## Slide 6
the high quality standard of whey required for further processing, optimum separation is essential. Therefore, in view of today's large whey volumes, the treatment processes must be designed so that the whey obtained is processed efficiently as far as possible in contained process lines without long holding times. In the case of semi-hard and hard cheeses, the suspended cheese fines content of the raw whey is 0.05% to 0.2% and, in the case of soft cheese, the value is up to 1.0%.
The large quantities of sediment can be handled by a skimming separator with only limited efficiency, even with large disc interspaces. Due to the greater distance between a smaller number of discs, the separation efficiency is effectively lower. The separa- tion efficiency is further affected by the behaviour of cheese fines in the disc stack. Cheese fines normally have two unpleasant characteristics:
most show a tendency to stick on metal surfaces
a large portion are often so fine that they can be separated only under the action of high centrifugal force.
The remaining cheese fines in the whey cause a rapid build-up of deposit on the separator discs, resulting in a drastic reduction of separation efficiency. In the past, the majority of whey separa- tion lines were equipped with only a screen to protect the separator. The screening technique, which is still used in some factories, is capable of removing only 30-60% of the cheese fines in the raw whey.
In such an installation, it is quite often necessary to incorporate intermittent cleaning cycles during a production run. In modern whey separation in- stallations, a clarifier replaces the whey screen.
The raw whey silo must be equipped with a spe- cially designed agitator, which helps to keep the cheese fines in suspension, to ensure that the flow to the centrifuge is constant. The whey is fed to the clarifier by means of a centrifugal pump. The feed rate is indicated on a flow meter and kept constant by means of a regulating device. The clarifier reduces the cheese fines to values smaller than 30-50 mg kg-1 in the finished whey. With such an installation, constant separation efficiency over the whole production run is guaranteed.
Fresh Cheese
Large-scale production of fresh cheese has been made possible only with the aid of centrifuges. Both separator design and process development are equally important for the efficiency and economical
production of fresh cheese. Fresh cheese is the precipitated and concentrated curd from cheese milk, with seasoning and other additives. Fresh cheese is not subject to a ripening process after pro- duction. Typical products are quark (petit suisse, fromage frais), cream cheese and double cream cheese. Fresh cheese centrifuges are especially de- signed for these products. A very high g force, which can be accomplished with special nozzle-type cent- rifuges, also ensures that the denatured (thermo- quark process) whey proteins are separated out efficiently with the cheese.
A high-fat cheese, like double cream cheese, can be separated only with a specially designed centrifuge, which separates the cheese towards the centre of the bowl and the whey to the periphery. The cheese is lighter than the whey because of the high fat level and is discharged from the bowl by means of a centripetal pump.
Quark separators Separators of types KDA, KDB and KDC are equipped with a disc-type bowl with nozzles on the outer rim for discharge of the con- centrate (quark). The segment-holding insert, shown in Figure 7, is sealed against the cover and the bottom part of the bowl. The stainless-steel segments prevent the accumulation of protein particles inside the bowl (Figure 7).
All protein particles separated out in the bowl are guided to the nozzles and discharged as quark. This design prevents quark losses from forming residues in
Figure 7 Stainless-steel segment holding insert in bowl bottom to prevent formation of protein segments.
CENTRIFUGES 249

## Slide 7
the bowl. It also allows longer processing times between clean-in-place (CIP) cleanings.
The coagulated skim milk enters the centre of the bowl through the feed tube and flows over the distributor into the rising channels of the disc stack, where it is separated into quark and whey. The whey flows inwards through the disc interspaces, while at the same time residual protein particles are separated out. The whey is then discharged by a centripetal pump in the bowl top. A sight glass is fitted in the whey discharge line so that separation can be moni- tored. If the whey becomes turbid, then all para- meters important for separation, such as feed throughput, separation temperature, treatment of the cheese milk and the dry matter content of the quark must be checked.
The separated quark is discharged continuously through nozzles into the concentrate catcher. Once the bowl has come to a standstill, the nozzles can be changed after removal of a locking piece on the hood.
The quark flowing out of the nozzles runs down
the chilled water cooled hood, over the chute into the quark hopper of the separator. Level sensors in the quark hopper control the operation of the quark pump.
Separator type KSA For the production of double cream cheese, the coagulated, standardized milk is fed into the centre of the bowl through the feed tube. From there, the milk is guided through the distributor into the rising channels of the disc stack, where it is separated into cheese and whey. The whey flows outwards through the disc interspaces, while the residual protein-fat particles are simultaneously separated out.
The whey flows through the separating disc into the upper pump chamber and is discharged foam-free under pressure by the centripetal pump.
Because of its high fat content, the cheese forms the light phase and flows inwards, where it is con- centrated. It then flows over a weir (regulating disc) into the lower pump chamber. The concentrate centripetal pump conveys the cheese to the outlet.
The dry matter content of the cheese is adjusted by means of a valve in the whey discharge. If the
discharge pressure is increased, more cheese is forced out of the bowl and the dry matter content is reduced.
If the dry matter content of the cheese is to be in- creased, the discharge pressure of the whey must be reduced.
During production, a small amount of free protein (inadequately weighted by fat) is separated out into
the sediment-holding space. This protein is ejected from the bowl in partial desludgings at intervals of approximately 2 h.
A sight glass is fitted in the whey discharge line for monitoring separation. If the whey becomes cloudy, then a partial desludging should be carried out. If this does not improve the situation, then parameters such as separation temperature, cheese milk treatment and the dry matter content of the cheese should be checked.
Removal of Bacteria
The first steps towards centrifugal removal of bacteria can be traced back to the 1950s but suc- cessful industrial use of this technology was perfected only in the 1970s. The great technological break- through made in the 1980s increased efficiency due to advanced design and high throughput cap- acities, which were the factors of integrating this technology in more and more cheese process lines. A further development of this technology in the 1990s, involving a reduction in the volume of con- centrate, made it suitable for many dairy process lines and product technologies. The bacteria con- centrate being discharged has been reduced to a very low level.
The well-known pasteurization process (heating at
72-75 oC for 15-30 s) to kill pathogens has been used for many decades in dairy plants. Unfortunately, the higher temperature needed to kill thermophiles adversely affects the flavour of milk and the func- tionality of the milk components. Even with the use of higher temperatures, as described above, the heating process does not eliminate all undesirable bacteria.
The removal of bacteria from milk and milk prod- ucts can be seen as an important processing stage in today's dairy plants, especially when taking into account that milk collection, processing and distri- bution procedures have changed markedly during the last decade as a result of the amalgamation of large dairy companies with 24-h operations. Nowadays, milk is collected only every second or third day and is stored for up to 24 h in the dairy prior to processing. Also, consumers are more demanding and expect milk and milk products to last longer without deteri- oration of flavour and colour.
A further example is the liquid milk industry where without clarification to remove bacteria, it is neces- sary to process milk every day in order to achieve a shelf-life of up to 2 weeks. With clarification, an extension of the shelf-life by 25% can be achieved, which can simplify processing and distribution of the
250 CENTRIFUGES

## Slide 8
product considerably. This is very important for the consumer.
For some processes, such as cheesemaking, it is very valuable to be able to process milk in which the bacterial count is very low or has been greatly re- duced. In some cases, it is necessary to reduce the numbers of bacteria or spores by as much as 99% to ensure a cheese with good quality. It is normally not possible to heat milk to such a degree that spores can be killed because such heat treatment may give a lower yield of cheese and can also adversely influ- ence the rennet coagulation time. Conventionally, additives have been used to reduce this problem. However, in most cases today, it is desirable to avoid the use of such additives.
Summarizing, it can be stated that the conventional systems (pasteurization, cooling, additives, steam injection, etc.) do not completely kill the spores of Clostridium and Bacillus species and, in addition, most treatments have side effects. It should also be mentioned that, generally, milk has higher contents of spores during the winter months when cows are fed on silage.
Bacillus cereus is often the predominant bacterial species in conventionally processed milk of advanced age, as it survives the pasteurization process and grows at low temperature, causing spoilage of the milk.
The damage that spores can cause to the industry can be considerable and the following examples are
affected:
fluid milk: reduction of shelf-life due to sweet (nonacid) precipitation
milk powder: aerobic and anaerobic spores (Bac. cereus, Clostridium perfringens) can cause dam- age, especially to low-heat milk powder
cheese: lactate-fermenting bacteria (anaerobic
spores) can cause late blowing of cheese.
The process with integrated bacterial centrifuge (bactofuge) Before the end of the 1980s, approxim- ately 3% by volume of feed was ejected as bacterial concentrate. In order to reduce the loss of product this secondary stream was sterilized and added back to the main stream. In some applications, and depending on the request, this process is still used today. At the end of the 1980s, the method of recycling a large part of the bacterial concentrate was introduced and widely accepted by the dairy industry. Design changes in the bowl resulted in the flow of a second liquid stream, the so-called 'carrier liquid', via the separa- tion disc, through nozzles, into the upper centripetal pump chamber where it is discharged foam-free under pressure from the separator.
By means of the latest technology, a large con- tinuous flow of carrier liquid conveys the bacteria into a high g force area in the clarifier. This process was developed and patented by Westfalia Separator. The amount of carrier liquid to be recirculated must be regulated according to the composition of the raw milk. Our experience has shown that 3-5% of the feed to the centrifuge should be recycled.
The above-mentioned system has the following advantages:
gentle handling of the product via the so-called soft stream feed system means that disruption of the bacterial colonies does not occur in the inlet
stagnation points are avoided and at the same
time flow velocities greater than 1.5 ms-1 are assured
the separating disc is designed to be positioned in the sediment-holding space of the bowl
the adjustable volume of the carrier liquid can be
set so that the bacterial count is roughly the same as in the untreated milk or, at maximum, twice as high
a precise ejection system is provided by an
optimized hydraulic system for fast opening and closing of the bowl (moving of the sliding piston).
With the above-mentioned system, only the ejected concentrate (by partial discharges) needs to be sep- arately treated. This volume is only 0.1-0.3% of the feed to the centrifuge, which in most cases is dis- regarded. The small volume does not economically justify the recovery of this secondary stream.
See also: Liquid Milk Products: Pasteurized Milk. Membrane Separation. Process and Plant Design. Whey Processing: Utilization and Products.
Further Reading
Renner E (1988) Lexikon der Milch. Munich, Germany: VV-GmbH Volkwirtschaftlicher Verlag.
Sienkiewicz T and Riedel C-L (1990) Whey and Whey Utilization, 2nd rev. edn. Gelsenkivoken, Germany:
Verlag Th. Mann.
Westfalia Separator (1991) Processing Lines for the Production of Soft Cheese, 3rd edn. Oelde, Germany:
Westfalia Separator Co.
Westfalia Separator (2000) Separators for the Dairy Industry, 5th rev. edn. Oelde, Germany: Westfalia Separator Co.
CENTRIFUGES 251