## Slide 1
Types of Agitators
Several types of agitators are used in dairy processing and these can be broadly classified based on the viscosity of the product.
Propeller Agitators
The three-bladed marine impeller (Figure lA) is a high-speed agitator (400-1750 rpm) with a small impeller-to-tank diameter ratio (0.2-0.3). It is used
to agitate low viscosity liquids (usually < 1 Pa s) wherein the momentum generated by the impeller is easily transferred throughout the liquid. It produces an axial flow pattern (Figure lB), which gives reasonable mixing and good suspension of particles.
Turbine Agitators
These agitators have an impeller to tank diameter ratio in the range of 0.2-0.5, and can be operated at a high speed if required. They are used to agitate low viscosity liquids (usually < 1 Pa s), but they have also been used to agitate liquids with a viscosity as high as 50 Pa s. The basic turbine is a flat-blade design and one of the most common turbines is the six flat- bladed disc-mounted impeller (Figure 2), which is often used in fermentors. Turbine impellers can
AGITATORS IN MILK PROCESSING PLANTS 1
A
Alatoxins see Mycotoxins: Afatoxins and Related Compounds.
AGITATORS IN MILK PROCESSING PLANTS
D A MacCarthy, J J Fitzpatrick and K Cronin, University College, Cork, Republic of Ireland
Copyright 2002, Elsevier Science Ltd. All Rights Reserved
Introduction
There are many reasons for the agitation of milk and milk products, including: (1) to maintain product uniformity; (2) to promote heat transfer; and (3) to disperse and dissolve solids in water. However, excess agitation is to be avoided, as it can cause product damage by disrupting the fat globule membrane and exposing the fat to lipase. Overagitation can also cause the formation of butter granules and non- globular fat.
The types of agitators that are commonly used in the dairy industry are described below. The mechan- ical and hygienic design of such systems is outlined and the issues involved in the selection and sizing of a particular agitation system are presented. Heat transfer in agitated vessels is explained and an over- view of the applications of agitation in milk pro- cessing is described.
(A)
(B)
Figure 1 (A) Three-bladed marine propeller, showing typical fow pattern for side entry; (B) the axial fow pattern it produces.

## Slide 2
induce strong radial flow in addition to axial flow, which imparts a much greater mixing capability than propeller agitators. Pitch-bladed turbines have their blades set at an angle of less than 900 from the hori- zontal (Figure 3) and are used in the dairy industry, for example, in lactose crystallization and yoghurt manufacture. The smaller the angle, the milder the agitation as less shear forces are exerted on the liquid and on any particles or droplets within the liquid.
Paddle Agitators
The basic paddle agitator resembles the basic turbine agitator except that it has a larger impeller to tank diameter ratio ( > 0.5 to < 1) and rotates at a low speed, typically 10-150 rpm. Paddle agitators are used in the dairy industry to agitate medium viscosity liquids (0.5-10 Pa s). Increasing the viscosity will dampen the momentum transfer through the liquid and thus greater contact between the impeller and the liquid is required, which results in larger diameter
High-Viscosity Agitators
Helical and ribbon-type agitators are used to agitate very high viscosity liquids (up to 1000 Pa s).
Air Agitation
Milk kept in large storage tanks may be agitated by supplying compressed air near the base of the tank. The air bubbles rise, expand and set up circulation currents in the milk. The air supply is regulated using a level detector, which matches the air flow-rate to the quantity of milk in the tank.
Figure 3 Pitched three-bladed impeller.
Figure 4 Paddle impellers: (A) basic paddle; (B) anchor;
(C) gate and (D) anchor-gate.
impellers with greater contact area. There are many variants of the basic paddle (as illustrated in Figure 4) which give greater contact area. Some of these, such as the gate-anchor agitator, can be used with high viscosity liquids up to around 100 Pa s.
High-Shear Agitators
High-shear mixers are used to break up particles such as in powder reconstitution or emulsion droplet formation. Rotor-stator agitators (Figure 5) are commonly used; the product is drawn into a high- speed rotor, typical speed 3000 rpm, in a closely machined stator, in which the solids are subject to milling and intensive hydraulic shear. This may be done batchwise in a mixing vessel, or in-line for continuous blending. Powder mixing systems are commercially available, incorporating powder hopper, venturi feeder and in-line mixer.
Figure 2 Six-bladed disc turbine impeller showing typical fow pattern for centre axial entry.
(D)
(C)
(B)
(A
Figure 5 High-shear rotor-stator impeller.
2 AGITATORS IN MILK PROCESSING PLANTS
) |  |  | 

## Slide 3
Mechanical Design
The agitation system consists of an electric motor which transmits power through a mechanical drive system. The drive system consists of a power transfer unit (gearbox or belt drive), shaft and impeller, bearings and seals. Figure 6 illustrates in schematic form the basic system configuration.
Electric Motor and Gearbox/Belt Drive
Electric motors will rotate at an angular velocity (normally 1500 or 3000 rpm) that is too high for the agitator impeller. Thus, a power transfer unit that allows a reduction in rotational velocity will be needed in the system, as in many cases impeller angular velocity will be less than 100 rpm. In the special case where a power transfer unit is not required, the system is referred to as direct drive. Two of the most common types of power transfer unit are the gearbox and belt drive. Gearboxes have the advantage of high torque transmission capability, high dimen- sional accuracy and low friction losses, and they predominate in dairy processing. In many cases, the electric motor and gearbox is supplied as a unit. Belt drives are a flexible power transfer unit with the features of quiet running and good vibration damp- ing properties. They are limited by (relatively low) operating temperatures and speeds and are not very common in dairy agitation systems.
Drive Shaft
The drive shaft transmits mechanical power from the electric motor to the impeller. In tall tanks, it may be necessary to fit more than one impeller at different levels on the stirring shaft in order to obtain the
required effect. The number of impellers required is approximately equal to the ratio of tank height to tank diameter. It will be necessary to support this shaft with bearings in order to minimize friction, wear, noise, deflection and vibration. Bearings can be classified as being journal (plain) bearings or rolling bearings; the latter are generally used.
A variety of arrangements to introduce the impeller shaft into the process vessel are possible. The shaft can enter the vessel from the top (top mounted), from the bottom or from the side. The shaft can be parallel, perpendicular or inclined to the vessel longitudinal axis. Top-mounted vertical agitator drives are most common, with the shaft either coaxial or eccentric (off-centre) with respect to the vessel axis. Bottom or side entry may be advantageous if more space is needed at the top for entry ports and manifolds or if headspace is limited. The shaft can run the full length of the vessel and be supported by bearings at either end (top and bottom) or can terminate at the impeller and be supported by a bearing at the point of entry into the vessel.
Sealing
Satisfactory sealing of the rotating agitator shaft is essential for hygienic operation and yet difficult to achieve. As an example, for top-mounted systems, the dripping of lubricant oil from the gearbox into the tank contents is not acceptable even if a food-grade lubricant oil is specified. Any sealing arrangement must be able to resist the appropriate sterilizing temperature. The most common type of dynamic seal is the axially loaded face seal (mechanical seal). Note that O rings should, generally, be avoided in food contact equipment.
Steam in
Steam out
Steam shroud
Seal faces
Ball bearing
Rotating collar fixed to shaft
Impeller
Figure 6 Drive system for top-mounted agitator.
Rotating driveshaft
Electric motor
Reduction gearbox
Fixed vessel top plate
Spring
AGITATORS IN MILK PROCESSING PLANTS 3

## Slide 4
A mechanical seal consists of a pair of rings, one stationary and the other rotating with the shaft. They are spring-loaded together and dynamic seal- ing takes place between their flat annular surfaces. Mechanical seals may be carbon rings (graphite) rubbing on carbon rings or silicon carbide on sil- icon carbide. Silicon carbide is a ceramic material, which is harder than graphite and thus gives a longer seal life. High temperature, low friction plastics, such as Teflon (PTFE), are also used. Mechanical seals with silicon carbide/carbon running surfaces are inert under operating conditions normally en- countered and are considered to be safe in food processing. Steam barriers may also be used to further guarantee containment.
Hygienic Design
Hygienic design of the agitator system involves the consideration of issues that include materials of con- struction, cleanability and surface finish. As food contact surfaces, which must remain inert, impervious and durable, the shaft and impeller will in all likeli- hood be built from stainless steel. There are many grades of stainless steel, but the austenitic grades AISI 304 or AISI 316 are the most common in dairy applications. Misuse of sterilizing agents (chlorite bleaches) can cause corrosion of stainless steel (see Corrosion). It is for this reason that grade 316 may be preferred with its higher resistance to corrosion attack from chloride ions. This also highlights the need for careful water rinsing in the cleaning cycle to ensure that the concentration of chloride ions in inaccessible places, such as any machine crevices, is not allowed to reach dangerous levels.
The surface finish of the agitator affects the ability to clean, sanitize and sterilize the shaft and impeller. Surface finish can be quantitatively measured by the arithmetic mean roughness (Ra) number. Generally, dairy contact surfaces should have an Ra of less than
0.8 µm and such a finish is obtainable by mechanical and electropolishing.
Agitator Selection and Sizing
Viscosity
Viscosity is the resistance of a liquid to flow. Low viscosity liquids show little resistance to flow and thus liquid momentum is easily transferred throughout the liquid and low power is required to agitate the liquid. On the other hand, high viscosity liquids have a high resistance to flow whereby viscous forces dampen liquid momentum transfer and require higher power to agitate the liquid. In addition, many dairy liquids
are non-Newtonian, and are mainly pseudoplastic,
i.e. viscosity decreases with increasing shear rate. This results in higher viscosities in regions of the liquid that are more remote from the impeller, which may lead to poor mixing in these regions. Typical values for the viscosity of some dairy liquids are presented in Table l at specified temperatures, as viscosity is usually a strong function of temperature.
Agitator Selection
Selection of agitator type is determined by the viscos- ity of the liquid and the agitation job to be per- formed, whether it be mixing, heat transfer, particle dispersion, oxygen transfer or a combination of these. Each agitator type has a range of viscosities at which it performs best and agitation duty for which it is best suited, as mentioned above. Equipment suppliers and process design companies have the experience and practical knowledge for selecting an appropriate agitator to perform a specified job.
Agitator Dimensions and Speed
Once an agitator type is selected, it has to be sized in terms of its dimensions. This will depend on the size of the tank and the volume to be processed. For a given impeller type, there are standard geo- metrical configurations for the impeller and tank, which give guidance to sizing the impeller. For most agitation applications, with the exception of heat transfer, there is no well-developed mathematical analysis supported by property data that can be used to evaluate the effect of impeller speed and diameter on agitation performance. In these cases, it is necessary to evaluate on a small/pilot scale how impeller speed and diameter affect agitator performance and then scale up these results. Impeller tip speed is usually constrained in dairy processing because of its effect on product quality.
Table 1 Typical viscosity of dairy liquids
Liquid
Temperature (0C)
Viscosity (Pa s)
Low viscosity Water Whole milk
Skim milk concentrate (33% solids)
20
20
25
1(10-3)
2(10-3)
3)
13(10-
Medium viscosity
Yoghurt
Milk concentrate (48% solids)
Whey concentrate
10
20
1-4
1
(65% solids)
10 5
4 AGITATORS IN MILK PROCESSING PLANTS

## Slide 5
Agitator Power Requirement
There are many power curve correlations available in the literature for estimating the power require- ment for specific impeller tank configurations, and these are usually presented in the form of power number or function versus Reynolds number, as illustrated in Figure 7. Once the impeller speed and diameter, liquid density and viscosity are known, the Reynolds number can be calculated. The power number can be read from the power curve for the specific impeller tank configuration, and the power requirement can be calculated from the Power number or function. Separate curves are required for baffled and unbaffled systems due to possible vortex formation in unbaffled systems. As a general guide, typical mixing power consumption varies from 0.2 kW m-3 for low viscosity liquids up to 4 kW m-3 for blending materials with the consist- ency of pastes and doughs.
Vortexing
Tangential flow in the direction of rotation of the impeller can lead to vortex formation when agitating low viscosity liquids by centrally mounted impellers in unbaffled tanks. Vortexing due to increasing rotational speed may lead to air entrainment by exposing the impeller to air. This can also produce large oscillating forces acting on the impeller shaft. Vortexing can be prevented by mounting the impel- ler off-centre or using a horizontal side-entering
impeller. There are cases where vortexing is advant- ageous, for example, in powder reconstitution. When powder is added to the surface of water, the vortex can greatly improve powder sinkability by centri- fugally spinning the powder into the water, and this becomes even more important as the solids content of the reconstituted mixture increases.
Heat Transfer in Agitated Vessels
Heat transfer coefficients for the heating or cooling of a liquid in a jacketed vessel may be calculated using the correlation:
Nu = aReb Prc(µ/µW)d
where
Nu = hDT/k Re = DA2Np/µ Pr = Cp µ/k
h = heat transfer coefficient (product) (W m-2 K)
k = thermal conductivity (W m-1 K)
DT = tank diameter (m)
DA = agitator diameter (m)
1)
N = rotational speed (s-
p = density (kg m-
3)
Cp = specific heat (J kg-1 K)
µ = viscosity (Pa s)
µW = viscosity at wall temperature (Pa s)
Values of a, b, c and d depend on system geometry.
100
101
102
103
104
105
100
Power number N P =
101
102
P
pN 3D 5
Reynolds number N =
Re
pN 2D
µ
Figure 7 Power curve correlation for estimating agitator power requirement.
AGITATORS IN MILK PROCESSING PLANTS 5
Laminar |  |  |  |  |  |  |  | Transition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Turbulent |  |  |  |  |  | 

## Slide 6
Heat transfer in a jacketed vessel may sometimes be problematic when dealing with medium and high viscosity liquids because of low heat transfer rates and the formation of deposits on the tank wall. This is overcome by using paddles with a small clearance between the impeller and the tank wall so that the blade surfaces sweep the wall of the tank clearing away any deposits and preventing a stagnant layer at the wall surface.
Applications
On-Farm
Following milking, milk is stored in refrigerated tanks pending milk collection and delivery to the dairy. Agitation is required for two purposes: to improve heat transfer while the milk is being cooled, and to avoid fat separation and facilitate milk sampling for analysis and payment. Typical agitation system: paddle agitator, motor about 100 W, geared down to about 30 rpm. The agitator will operate continuously during cooling, and intermittently (e.g. 30 s every 15 min) during storage.
Milk Intake
When milk is received at the dairy, it is stored as raw or pasteurized milk. Agitation is required at this stage to maintain uniform composition for downstream pro- cessing and inventory control. Typical agitation sys- tems include: (1) top-entry agitator with more than one pitch-bladed impeller; (2) side-entry agitator, marine propeller, angled down from the horizontal; and (3) air agitation, which is less commonly used because incorporation of air in milk can lead to problems in heat exchangers and centrifuges. In modern installa- tions, provision is made to inactivate the agitator when the product surface is at the height of the agitator.
Cream Storage
Agitation of cream should be more gentle than agitation of milk because of the greater possibility of product damage. Typical agitation: pitch-bladed or paddle impeller, speed 30-60 rpm.
Milk and Whey Concentrates
Milk concentrates are produced by evaporation for dehydration, or by the addition of solids for yoghurt or ice cream manufacture. These products can be effectively agitated using marine propeller or pitch- bladed agitators at 200-400 rpm.
Powder Dispersion
The dispersion of powders in water is required for the manufacture of many dairy products including ice
cream, yoghurt, dairy spreads and dairy desserts. Complete dispersion of the solids in the aqueous phase is required, with no residual lumps and without air incorporation. Particular difficulty is encountered in dispersing stabilizers, e.g. guar gum and locust bean gum, and emulsifiers, e.g. mono or diglycerides. This is usually achieved using high-shear mixers.
Yoghurt
Yoghurt is characterized by a high solids content (about 20%) and medium to high viscosity depend- ing on whether the yoghurt is stirred or set. Gentle agitation is required to avoid damage to product texture. This can be achieved by using a top- mounted agitator with large paddles and a speed of 20-60 rpm.
Processed Cheese
Processed cheese manufacture is characterized by high viscosity, dispersal of solids and high heating rates. Agitation is achieved by an anchor-type scraped- surface agitator, at a speed approximating 100 rpm.
See also: Hygiene in Dairy Production and Processing. Milking and Handling of Raw Milk: Milking Hygiene; Effects of Storage and Transport on Milk Quality. Process and Plant Design.
Further Reading
Cowan CT and Thomas CR (1988) Materials of construc- tion in the biological process industries. Process Biochemistry 23(1): 5-11.
Hall CW, Farrall AW and Rippen AL (1986) Encyclopedia of Food Engineering. Westport: AVI.
Hauser G (1992) Hygienic design of moving parts of
machines in the food industry. Transactions of the
Institute of Chemical Engineering 70(part C): 138-142. Holland FA and Chapman FS (1966) Liquid Mixing and
Processing in Stirred Tanks. New York: Reinhold.
Kessler HG (1981) Food Engineering and Dairy Techno- logy. Freising, Germany: Verlag A. Kessler.
Oldshue JY (1985) Mixing processes. In: Bisio A and
Kabel RL (eds.) Scaleup of Chemical Processes. New York: John Wiley.
Perry RH and Green DW (1997) Chemical Engineers'
Handbook, 7th edn. New York: McGraw-Hill.
Stanbury PF, Whitaker A and Hall SJ (1995) Principles of Fermentation Technology. Oxford: Butterworth- Heinemann.
Tetra Pak (1995) Dairy Processing Handbook. Lund, Sweden: Tetra Pak.
Uhl VW and Gray JB (1966) Mixing: Theory and Practice.
New York: Academic Press.
6 AGITATORS IN MILK PROCESSING PLANTS