## Slide 1
All figures taken from Design of Machinery, 3rd ed. Robert Norton 2003
MENG 3071 Chapter 2
Position Analysis

## Slide 2: Coordinate Systems
Cartesian (Rx, Ry)
Polar (RA, q)
Converting between the two
Position Difference, Relative position
  Difference (one point, two times)
  relative (two points, same time)
RBA=RB-RA
X
Y
RB
RA
A
B
RBA

## Slide 3: 4.3 Translation, Rotation, and Complex motion
Translation: keeps the same angle
Rotation: one point does not move
Complex motion: a combination of rotation and translation

## Slide 4: Graphical Position Analysis of Linkages
Given the length of the links (a,b,c,d), the ground position, and q2. Find q3 and q4
a
d
q2
b
c
q3
q4
A
B
O2
O4
b
c

## Slide 5: Graphical Linkage Analysis
Draw an arc of radius b, centered at A
Draw an arc of radius c, centered at O4
The intersections are the two possible positions for the linkage, open and crossed
a
d
q2
b
c
q3
q4
b
c
A
O2
O4
B1
B2

## Slide 6: Algebraic Position Analysis
Obtain coordinates of point A:
Obtain coordinates of point B:
These are 2 equations in 2 unknowns: Bx and By
See solution in textbook pages 171, 172.

## Slide 7: Complex Numbers as Vectors
We can plot complex numbers on the real-imaginary plane
Euler identity e±iq=cos q ± i sin q
Cartesian form: RAcos q + i RAsin q
Polar form: RAeiq
Multiplying by eiq corresponds to rotating by q
Real
Imaginary

## Slide 8: Analytical Position Analysis
Given: link lengths a,b,c and d, q1, q2 (the motor position)
Find: the unknown angles q3 and q4

## Slide 9: Analytical Position Analysis
Write the vector loop equation:
(Positive from tail to tip)
Substitute with complex vectors
Take knowns on one side, unknowns on the other.
Call the knowns Z
Unknowns
Knowns

## Slide 10
Fourbar Linkage Analysis
Define:
Take conjugate to get a second equation:
For the conjugate of s we have (only true for eiq)
So our second equation is
Note:

## Slide 11: Fourbar Linkage Analysis
Quadratic equation in t
Use algebra to eliminate one of the unknowns
Multiplying the two gives:
Multiplying by t and collecting terms gives:
From the quadratic formula

## Slide 12: Fourbar Linkage Analysis
In MATLAB,
Zc=conj(Z)
t=roots([Zc*c,Z*Zc+c^2-b^2,Z*c])
q4=angle(t), q3=angle(s)
Two solutions relate to the open and crossed positions
a
d
q2
b
c
q3
q4
A
O2
O4
B1
B2

## Slide 13
Change your current directory
Type in your commands here … or
Use a text editor
MATLAB

## Slide 14
>> a=2; b=3; c=4; d=5;
>> th1=0; th2=60*pi/180;
>> z=-a*exp(i*th2)+d*exp(i*th1)
z =
4.0000 - 1.7321i
>> zc=conj(z)
zc =
4.0000 + 1.7321i
>> t=roots([zc*c,z*zc+c^2-b^2,z*c])
t =
-0.4194 + 0.9078i
-0.9490 - 0.3153i
>> s=(z+c*t)/b
s =
0.7741 + 0.6330i
0.0680 - 0.9977i
>> th4=angle(t)*180/pi
th4 =
114.7975
-161.6240
>> th3=angle(s)*180/pi
th3 =
39.2750
-86.1015
b
c
q3
q4
A
B
a
d
q2
O2
O4

## Slide 15: Animation on MATLAB
% *******************************
% Animation of a four-bar linkage
clear; close all;
% Define parameters (link lengths)
a = 1; b = 3; c = 4; d = 5; th1 = 0;
% Now loop on the crank angle
for th2 = 0:0.05:2*pi
z = -a*exp(i*th2)+d*exp(i*th1);
zc = conj(z);
t = roots([zc*c,z*zc+c^2-b^2,z*c]);
s = (z+c*t)/b;
th3 = angle(s);
pA = a*exp(i*th2); % Position of point A
pB = pA+b*exp(i*max(th3)); % Be careful here!
% We took max(th3) because that will give the 'open' position.
% This may not work for all cases, so watch out!
% Now plot and animate. Fix the axis limits to see the animation.
plot([0 real(pA) real(pB) d 0],[0 imag(pA) imag(pB) 0 0],'linewidth',8);
axis([-1.2*a 1.2*d -c c]);%axis off
pause(0.01)
end

## Slide 16: Inverted Crank Slider linkage
Given: link lengths a, c and d, q1, q2 (the motor position), and g the angle between the slider and rod
Find: the unknown angles q3 and q4 and length b

## Slide 17: Inverted Crank Slider linkage
Write the vector loop equation
Substitute with complex vectors
Geometry keeps
so

## Slide 18: Inverted Crank Slider
Grouping knowns and unknowns
Calling
Gives
Taking the conjugate to get the second equation
Multiplying the two gives

## Slide 19: Inverted Crank Slider
The solution is a quadratic equation in b
Which has a solution of
b=roots([1 c*(t+1/t),c^2-Z*Zc])
Once b is known, s can be found using

## Slide 20: Crank Slider Mechanism
Given: link lengths a, b and c, q1, q2 (the motor position)
Find: the unknown angle q3 and length d

## Slide 21: 4.8 Linkages of More than Four Bars
Geared fivebar linkage
vector loop equation
Complex vectors
Separate unknowns and knowns (q5=lq2+f)
(same eqn.
as 4bar)

## Slide 22: Sixbar Linkages
Watt’s sixbar can be solved as 2 fourbar linkages
R1R2R3R4, then R5R6R7R8
R4 and R5 have a constant angle between them

## Slide 23: Sixbar Linkages
Stephenson’s sixbar can sometimes be solved as a fourbar and then a fivebar linkage
R1R2R3R4, then R4R5R6R7R8
R3 and R5 have a constant angle between them
If motor is at O6 you have to solve eqns. simultaneously

## Slide 24: Position of any Point on a Linkage
Once the unknown angles have been found it is easy to find any position on the linkage
For point S
Rs=sei(q2+d2)
For point P
RP=aei q2 +pei (q3+d3)
For point U
RU=d +uei (q4+d4)

## Slide 25: Using MATLAB (Spring 2007)

## Slide 26: Example
Given: a,c,d,q2
Find: position of point P (coupler curve)
b
In MATLAB:
z = a*exp(i*th2)-d;
b = abs(z); th3 = angle(z);

## Slide 27: MATLAB m-file
clear; close all;
a = 2.4; c = 13.4; d = 8;
cupcur = [];
for th2 = 0:0.1:2*pi
z = a*exp(i*th2)-d;
b = abs(z); th3 = angle(z);
rp = a*exp(i*th2)-c*exp(i*th3);
cupcur = [cupcur rp];
X = [0 real(a*exp(i*th2)) real(rp)];
Y = [0 imag(a*exp(i*th2)) imag(rp)];
plot(X,Y,'.-'); axis equal; axis([-5 20 -5 5]); grid; hold on;
plot(real(cupcur),imag(cupcur),'.r');hold off;axis off
pause(0.1)
end
Mt1f13.avi
b

## Slide 28: Transmission Angle
Extreme value of transmission angle when links 1 and 2 are aligned
Overlapped
Extended

## Slide 29: Toggle Position
Caused by the colinearity of links 3 and 4.
For a non-Grashof linkage, only one of the values between the () will be between –1 and 1
q2
q2
2
3
4
4
3
2
Overlapped
Extended