## Slide 1: Cadastral Surveying
Introduction

## Slide 2: Cadastre - Definition
cadastre is normally a parcel based, and up-to-date land information system containing a record of interests in land (e.g. rights, restrictions and responsibilities).
A cadastre, historically, has meant a record of land parcels, similar in meaning to tax maps.

## Slide 3: Cadastral Surveying
Cadastral surveying is the discipline of land surveying that relates to the laws of land ownership and the definition of property boundaries.
It involves interpreting and advising on boundary locations, on the status of land ownership and on the rights, restrictions and interests in property, as well as the recording of such information for use on plans, maps, etc.
It also involves the physical delineation of property boundaries and determination of dimensions, areas and certain rights associated with properties, whether they are on land, water or defined by natural or artificial features.

## Slide 4: Cadastral surveying cont’d
Cadastral surveys are generally performed to subdivide land into parcels for ownership under a land title and to re-establish boundaries of previously surveyed properties to determine the physical extent of ownership or to facilitate the transfer of the property title.
Cadastral surveys are used to document land ownership, by the production of documents, diagrams, sketches, plans, charts, and maps.

## Slide 5: Cadastre includes
A geometric description of land parcels linked to other records describing the nature of the interests the ownership or control of those interests and often the value of the parcel and its improvements.

## Slide 6: Ownership
Real property ownership is not the ownership of land; it is the designation as the authority to control an area. It is the ownership of “rights.”
The right to build upon, improve, inhabit, cultivate, deny access to others, and countless other rights are what is owned.

## Slide 7: Title
The collection of papers, recordings, and other documents that describe a transfer of the titled rights to a real property parcel are often referred to as the title.

## Slide 8: DEED
A deed is the written instrument that describes the assignment of the rights that are “owned” and the geographical limits of that assignment.
A deed is not the same as a title, although the words are often used interchangeably.
Although the limits of the rights of real property ownership are invisible, they must be identifiable. Every deed must communicate what rights are owned and where the boundaries or limits of those rights are.
It is folly to attempt to transfer rights in real property without adequately identifying and communicating the location of the limits of the rights conveyed.

## Slide 9: IDENTIFYING BOUNDARIES
East
North
Corners: Instead of defining the boundaries of the parcel by marking each step of a walking man, the end points of each side could be marked and the boundary could be defined as a straight land line between the end land points or corners.

## Slide 10: Classification of cadastre
primary function (e.g. supporting taxation, conveyancing, land distribution, or multipurpose land management activities);
the types of rights recorded (e.g. private ownership, use rights, mineral leases);
the degree of state responsibility in ensuring the accuracy and reliability of the data (e.g. complete state mandate, shared public and private responsibility);
location and jurisdiction (e.g. urban and rural Cadastres; centralised and decentralised Cadastres);
the many ways in which information about the parcels is collected ( e.g. ground surveys tied to geodetic control, uncoordinated ground surveys and measurements, aerial photography, digitizing existing historical records, etc.)

## Slide 11: Types of Cadastre
a) Fiscal cadastre
It records information for the purpose of property valuation and land taxation. Here, the basic information needed is location and value of the parcel. In this regard, there must be some sort of agreed upon valuation method that help determine the value of a parcel.

## Slide 12
b) Legal cadastre
It is a register aiming at identifying the legal owner and exact boundaries of the parcel. To establish legal cadastre it requires delineation of boundaries of the given parcel through surveying and mapping and thereby provision of legal rights. In this respect, legal cadastre is helpful in:
1. Defining property rights;
2. Describing the extent of property rights;
3. Supporting land transfer; and
4. Providing evidence of ownership.

## Slide 13
c) Multi-purpose cadastre
It is a relatively new approach of land information system which is reported to have been introduced after the Second World War. This land register system incorporates all the necessary information, at one source, which among others are information related to legal and fiscal cadastre, land use, buildings, infrastructures of under ground and overhead constructions, soil and other aspects of the given parcel. In many respects, multi-purpose cadastre seems to be an important type of land information system for it provides multitudes of information related to a given parcel.

## Slide 14: SIGNIFICANCE OF CADASTRE
Facilitating efficient and safe land transaction;
Providing security and protection
Minimizing disputes and litigations of land
Serving as a tool for assessing and taxing land
Providing the necessary information for planning purposes
Managing environmental issues;
Facilitating the implementation of land reform when necessary.
Registering and carrying out inventory of heritages which are found in urban centers; and
Registering tourist facilities

## Slide 15: Land Registration and Mapping in Ethiopia
By the end of 1907 Menelik II declared the country's first urban land- related proclamation.
The French are reported to have initiated cadastral works in Addis Ababa in the 1920s.
Ethiopian Mapping Agency (EMA) established in 1954
Since the 1960s the Authority has begun production of large scale maps for town planning.
In 1985 the Addis Ababa city administration launched cadastral project with the core objective of registering property for taxation purpose.

## Slide 16: History cont’d
Introduction of modern cadastral system in some major regional towns of the country -piloted cadastral projects in four regional capitals namely: Mekelle, Bahirdar, Awassa and Adama.
In 1998 in Mekelle, in 1999 Bahirdar and Awassa, and in 2000 in Adama.
These projects have been launched with the intention of establishing multi- purpose cadastre that could be updated constantly. By doing so municipalities could be able in establishing up-to-date data -base system which would be instrumental in managing their resources efficiently.

## Slide 17: Peer group assignment
Discuss and report real practice of cadastre system in your town, city or Keble
Discuss and report a cadastre system on the period of derg regime and the government on the power now.