## Slide 1
Chapter 4
Mixer design and scale -up
©Solomon Bogale

## Slide 2: Agitation/Mixing
Agitation refers to forcing a fluid by mechanical means to flow in a circulatory or other pattern inside a vessel.
Mixing usually implies the taking of two or more separate phases, such as a fluid and a powdered solid or two fluids, and causing them to be randomly distributed through one another.

## Slide 3: Mixing Process design
For design or consideration of mixing process should understand:
    mechanism of mixing
    scale-up criteria
    power consumption
    flow patterns
    mixing time/rates
    types of equipment available

## Slide 4: Mixing equipments:
Mixers for liquid-liquid, gas and/or solid in liquid (referred as fluid mixing)
Mixers for solid-solid (powders)
Mixers for semisolids or pastes

## Slide 5: Fluid mixing applications

## Slide 6: Fluid mixing applications
1. Blending of two miscible liquids, such as ethyl alcohol and water.
2. Dissolving solids in liquids, such as salt in water.
3. Dispersing a gas in a liquid as fine bubbles,
- such as oxygen from air in a suspension of microorganisms for fermentation or for the activated sludge process in waste treatment.
4. Suspending of fine solid particles in a liquid,
- in the catalytic hydrogenation of a liquid, solid catalyst particles and hydrogen bubbles are dispersed in the liquid.
5. Agitation of the fluid to increase heat transfer between the fluid and a coil or jacket in the vessel wall.

## Slide 7: Blending of miscible liquids

## Slide 8: Blending of immiscible liquids

## Slide 9: Blending of immiscible liquids

## Slide 10: Liquid-gas mixing

## Slide 11: Liquid-solid mixing

## Slide 12: Fluid motion

## Slide 13: Fluid Mixing Processes
Mechanical Agitation
Jet Mixing
Gas Sparging
In-line Mixing

## Slide 14: Agitation Tank
The impeller is the most important part
The motor rotates the shaft; impeller
Baffles are many times added to improve mixing
Circular tip
A level indicator
Inlet/Outlet pipe
Notes: Unbaffled mixing tanks often used:
in transition region
for sticky materials
where perfect cleaning is required
in large tanks where baffle effects are small
processes where it is not clear baffles have an effect on mixing performance

## Slide 17: Baffles
Unbaffled mixing tanks often used:
in transition region
for sticky materials
where perfect cleaning is required
in large tanks where baffle effects are small
processes where it is not clear baffles have an effect on mixing performance

## Slide 18: Baffles

## Slide 20
Agitation in an unbaffled vessel (left) leads to swirling flow with surface vortex formation and poor solids distribution, while standard baffling (right) with a pitched-blade turbine promotes axial flow that results in good solids distribution.

## Slide 21: Devices to produce agitation
IMPELLERS
  Three-blade propeller agitator
  Paddle (Turbine) agitators
  Helical-ribbon agitators
The performance for impeller mixer depends on:
  Creation of a current or stream of liquid which penetrate to all point of mixing vessel or tank.
  Turbulence movement to carry the current in all places of the tank.
Notes: Paddle Agitators
Often used at low speeds, between about 20 and 200 rpm.
Two-bladed and four-bladed flat paddles are often used.
The paddle agitator is ineffective for suspending solids
- since good radial flow is present but little vertical or axial flow.
An anchor or gate paddle is often used.
Turbine Agitator
Turbines resemble of multi bladed paddle agitators with shorter blades
used at high speeds for liquids with a very wide range of viscosities.
The turbines usually have four or six blades.
They are also useful for good gas dispersion;
- the gas is introduced just below the impeller at its axis and is drawn up to the blades and chopped into fine bubbles.
Often a pitched-blade turbine with only four blades is used in suspension of solids.

## Slide 22: Impellers to produce agitation
Pitched-blade turbine
Three-blade
Marine propeller
Straight-blade
turbine
Disk turbine
Concave-blade CD-6 impeller

## Slide 23: Impellers

## Slide 24: Axial Flow Impellers

## Slide 25: Marine Propellers

## Slide 26: Pitched Blade Turbine

## Slide 27: Hydrofoil Impellers

## Slide 29: Fluid flow around the blades
Details of the flow around turbine blades a) a Rushton turbine, b) a pitched blade impeller, c) a hydrofoil.
Notes: The detail of the flow behind the blades is interesting. Flow around the blade of a Rushton turbine separates with a pair of trailing vortices from the tips of each blade. These vortices, which are rather less developed in a turbine without a disc, are the locations of the greatest shear rates and most intense turbulence in the vessel (van'tRiet and Smith). In the fully developed turbulence region (Re > ~ 105) the power number of a radial flow turbine is about 5. Much of the energy is small scale turbulence associated with the vortices; this decays rapidly in the outflowing stream so that about 80% of the energy transmitted from the shaft is dissipated in about 20% of the vessel volume.

## Slide 30: Radial Flow Impellers

## Slide 31: Rushton Turbine, Smith Impeller

## Slide 32: Open Blade Turbine, Coil Impeller

## Slide 33: Low Clearance Impellers
Notes: Helical-Ribbon Agitator
used in highly viscous solutions
operates at a low rpm in the laminar region.
The ribbon is formed in a helical path and is attached to a central shaft.
The liquid moves in a tortuous flow path down the center and up along the sides in a twisting motion.
Similar types are the double-helical-ribbon agitator and the helical-screw impeller

## Slide 35: High Shear Impellers

## Slide 36
(1 Outer Flight)
(1 Inner Flight, 1 Outer Flight)
(2 Outer Flights)
(1 Inner Flight , 2 Outer Flights )

## Slide 37
The Elongated Paddle impeller provides a combination of axial upward and radial fluid flow. It, like the Anchor and Helical Impellers, operates in close proximity to the vessel wall.
The Marine Propeller is an axial flow impeller generally pitched for downward pumping action, however, upward pumping is also available. This impeller provides a high, uniform discharge and therefore is best suited for low viscosity liquid blending applications. *Vessel baffling may be required for optimum performance.

## Slide 39: Impeller Selection

## Slide 40: Impeller Selection

## Slide 41: Side Entering Mixers

## Slide 42: Side Entering Mixers
Flow patterns for side-entering propeller

## Slide 43: Impeller position
Flow pattern of propellers in an eccentric angle and off-centered position

## Slide 44
Off-center agitator mounting (left) reduces swirl in unbaffled vessels, while angled, off-center mounting (right) approximates the flow in fully-baffled vessels

## Slide 45: Portable Mixers

## Slide 46: Jet Mixers

## Slide 47: Motionless Mixers

## Slide 50
Lödige systems enable therefore the gentle mixing of sensitive products and the concerted shear introduction into the material

## Slide 52: Solid-Solid Mixing

## Slide 53: Material Properties Affecting Solid Blending

## Slide 54: Material Properties Affecting Solid Blending

## Slide 55: Material Properties Affecting Solid Blending

## Slide 56: Material Properties Affecting Solid Blending

## Slide 57: Material Properties Affecting Solid Blending

## Slide 58: Structured and Random Blend Structures

## Slide 59: Mechanisms of Solid Blending

## Slide 60: Mechanisms of Solid Blending

## Slide 61: Diffusion Blending

## Slide 62: Convection Blending

## Slide 63: Shear Blending

## Slide 64: Segregation (De-mixing)

## Slide 65: Segregation Mechanisms

## Slide 66: Sifting Segregation

## Slide 67: Fluidization Segregation

## Slide 68: Dusting Segregation

## Slide 69: Minimizing Segregation

## Slide 70: Design Practices for minimizing segregation

## Slide 71: Solid Blending Equipment

## Slide 72: Tumbler Blenders

## Slide 73
Industrial V Blender.
Industrial Ribbon Blender
Industrial Double Cone Blender.

## Slide 74: Double Cone Blenders

## Slide 77: V Blender

## Slide 80: Advantages

## Slide 81: Disadvantages

## Slide 82: Convective Blenders

## Slide 83: Convective Blenders

## Slide 84: Horizontal Ribbon, Paddle Blender

## Slide 85: Vertical Ribbon Blender

## Slide 90: Vertical Cone Screw Blender

## Slide 93
Single screw configuration
• Standard execution
• Variety of designs
Double screw configuration
• Reduced mixing times
• Improved heat transfer
Intensifier
• Provides additional mixing energy
• Can be combined with liquid spray devices
Cantilevered (no support)
Radial bottom locator
Ball head bearing

## Slide 95: Plow Mixer

## Slide 96: Plow Mixer

## Slide 97: Twin Shaft Paddle Blender

## Slide 98: Twin Shaft Paddle Blender

## Slide 100: Selection of Solid Mixer

## Slide 101: Silo Blenders

## Slide 102: Gravity Silo Blender

## Slide 103: Mechanical Silo Blender

## Slide 104: Pneumatic Blender

## Slide 105: Mixing of High Viscosity Materials and Pastes

## Slide 106: High Viscosity Mixing

## Slide 107: Mixing Mechanisms

## Slide 108: Mixing Challenges

## Slide 109: Viscous Mixing Equipment

## Slide 110: Mixer Design

## Slide 111: Single Planetary Mixer

## Slide 112: Double Planetary Mixer

## Slide 113: Double Arm Kneader Mixer

## Slide 114: Double Arm Kneader Mixer

## Slide 115: Pan Muller Mixer

## Slide 116: Single Screw Extruder

## Slide 117: Twin Screw Extruder

## Slide 118: Pug Mills

## Slide 119: Advances in Mixing Technology

## Slide 120: Design of Turbines
Notes: F. PROCEDURE
Given a tank, impeller, baffles and liquid (water or corn syrup) we will vary the shaft speed and measure the torque. This will be done using a large and then a small tank, and with and without baffles. From these we will calculate Np and Nre, and check Np vs. the value taken from the plot. Then we will run corn syrup and use the plot to calculate the viscosity. We will also determine the effect of baffles vs. no baffles on the torque and mixing efficiency as determined by the tracer injection method.
1. Fill the 4 L tank with water and remove the baffles. Mount the 4-bladed, flat-bladed impeller on the mixer shaft. The mixer shaft position is a fixed reference point in the horizontal plane. Center the torque table directly beneath the shaft. Center the tank on the torque table. The impeller should be located vertically so that it is halfway between the tank bottom and the water surface. Set the rotation direction to clockwise (CW). Increase the stirring speed slowly until a vortex forms that pulls air into the tank. This is the maximum speed for this configuration. Set the speed at zero and record the torque reading (which may not be zero). Then run at 10 speeds evenly spaced between 0 and the maximum speed, and record the torque reading at each speed. Repeat using other impellers and rotation senses. Convert the torque reading to torque (in N m) using the calibration data below.
2. Repeat the procedure above with baffles inserted in the tank, using water.
3. Repeat steps 1 and 2 using corn syrup. The maximum speed may be limited by the power available.
4. Repeat steps 1 and 2 using the 20 L tank filled with water.
5. Mount the 4-bladed flat-bladed impeller and insert in middle of the 20 L tank filled to the mark with tap water. Mount the conductivity transducer 1 inch above the tank bottom and 1 inch from the tank wall, connect to the conductivity meter, connect the meter to the computer, and load and start the QuickBASIC program for agitation data acquisition. Remove the baffle(s) from the tank. Set the speed at 20% of the speed that produces air ingestion. Inject 10 ml of KCl solution onto the plate at the top of the tank, at the same time starting the data acquisition program. Make 5 additional injections under the same conditions. The tank will now contain a dilute solution of KCl. Empty the tank and refill with tap water. Set the speed at 80% of the maximum speed and make an additional 6 runs. For each run record the torque reading.
6. Repeat the 12 runs of step 5 with baffles inserted in the tank.
7. If time permits, repeat some of the runs of steps 5 and 6 using the propeller, driving fluid in the upward and then downward direction.
F. REPORT
The report should describe concisely the goals of the work, what was done, and the results and conclusions. The raw data should appear in an Appendix, and plots of torque and power vs. stirring speed should be presented and discussed in the body of the report. The effect of viscosity, baffles, impeller design should be discussed, and the power consumption should be compared with correlations from the literature (McCabe, Smith and Harriot).
Specifically, does the torque as a function of stirring speed follow the prediction of theory? And, how close is the observed power to that predicted by the correlation?
Plots of tracer concentration as a function of time should also be presented, and the effect of impeller type, baffles, and stirring speed on the tracer concentration vs. time curves should also be discussed.

## Slide 121: Agitated Vessel
Power Used in Agitated Vessel
In the design of an agitated vessel, an important factor is the power required to drive the impeller.
Empirical correlations have been developed to predict the power required.
Reynolds number, is defined as:
Where:
Da = impeller (agitator) diameter (m)
N = rotational speed (rev/s)
ρ = fluid density (kg/m3)
µ = fluid viscosity (kg/m.s)

## Slide 122
Power consumption is related to fluid density ρ, fluid viscosity µ, rotational speed N and impeller diameter Da by plots of power number Np versus
The power number is defined as:
(SI)
(English)
Where P = power (J/s) or (W). In English units, P = ft.lbf/s.

## Slide 124
Power correlations for various impellers and baffles
(Geankoplis, 4th ed.)

## Slide 125
Curve 1. Flat six-blade turbine with disk but six blades); D/W = 5; four baffles each D/J = 12.
Curve 2. Flat six-blade open turbine; Da/W = 8;four baffles each D/J = 12.
Curve 3. Six-blade open turbine (pitched-blade) but blades at 450; Da/W = 8; four baffles each Dt /J = 12.
Curve 4. Propeller; pitch 2D four baffles each Dt /J = 10; also holds for same propeller in angular off-center position with no baffles.
Curve 5. Propeller; pitch = Da four baffles each Dt /J = 10; also holds for same propeller in angular off-center position with no baffles.
Curve 6. High-efficiency impeller; four baffles each Dt /J = 12.

## Slide 127: Power Consumption in Agitated Vessels

## Slide 128
Example 1 Power Consumption in an Agitator
A flat blade turbine agitator with disk having six blades is installed in a tank similar to Fig. 3.4-3. The tank diameter Dt is 1.83 m, the turbine diameter Da is 0.61 m, Dt = H, and the width W is 0.122 m. The tank contains four baffles, each having a width J of 0.15 m. The turbine is operated at 90 rpm and the liquid in the tank has a viscosity of 10 cp and a density of 929 kg/m3.
a) Calculate the required kW of the mixer.
b) For the same conditions, except for the solution having a viscosity of 100,000 cp, calculate the required kW.

## Slide 129
Solution
For part (a) the following data are given:
Using Eq. (1), the Reynolds number is:
Using Curve 1 in the Figure, since
Solving for P and substituting known values

## Slide 130
For part (b)
This is the laminar flow region. From Figure, Np = 14.
Hence, a 10,000-fold increase in viscosity only increases the power from 1.324 to 3.71 kW.

## Slide 131: AGITATOR SCALE UP
Maintain
constant power per unit volume
geometric similarity
Scale-up the laboratory-size or pilot-size agitation system to a full-scale unit.

## Slide 132: Agitator Scale-Up
Scale-up procedure:
Calculate the scale-up ratio R. Assuming that the original vessel is a standard cylinder with DT1 = H1, the volume is:
The ratio of the volume is
The scale-up ratio is then

## Slide 133
Using this value of R, apply it to all of the dimensions to calculate the new dimensions. For Example,
Da2 = RDa1, J2 = RJ1…
Determine the agitator speed N2, to be used to duplicate the small scale results using N1. The equation is:
Where n = 1 for equal liquid motion, n = ¾ for equal suspension solids and n = 2/3 for equal rates of mass transfer (which equivalent to equal power per unit volume, P1/V1 = P2/V2 ). This value of n is based on empirical and theoretical considerations.
4. Knowing N2, the power required can be determined.

## Slide 134
Example 2 Scale up of Turbine Agitation System
An existing agitation system is the same as given in Example 1a for a flat-blade turbine with a disk and six blades. The given conditions and sizes are DT1 = 1.83 m, Da1 = 0.61 m, W1 = 0.122 m, J1 = 0.15 m, N1 = 90/60 = 1.50 rev/s, ρ = 929 kg/m3 and µ = 0.01 Pa.s. It is desired to scale up these results for a vessel whose volume is 3.0 times as large. Do this for the following two process objectives:
a) Where equal rate of mass transfer is desired.
b) Where equal liquid motion is needed.

## Slide 135
Solution
Since H1 = DT1 = 1.83 m,
the original tank volume,
Volume V2 = 3.0 (4.813) = 14.44 m3.
Following the steps in the scale-up procedure:
The dimensions of the larger agitation system are as follows:
DT2 = RDT1 = 1.442 (1.83) = 2.64 m, Da2 = 1.442 (0.61) = 0.880 m, W2 = 1.442 (0.122) = 0.176 m and J2 = 1.442 (0.15) = 0.216 m.
For part (a), for equal mass transfer, n = 2/3 :

## Slide 136
Reynolds number
Referring to Figure, Curve 1 and NRe = 8.453 x 104, gives Np = 5.0
Using Np = 5.0

## Slide 137
For part (b), for equal liquid motion, n = 1.0
The value of 0.2752 kW/m3 is somewhat lower than the approximate guidelines of 0.8 to 2.0 for mass transfer.
The power per unit volume is

## Slide 138
Pumping Capacity: discharge flow rate from an impeller:
Tip Speed of an impeller:
Torque: “twist” force acting on
agitator shaft:
Power per unit volume:
Notes: Q = discharge flowrate, or pumping capacity.
For “square-pitched” propellers in turbulent region, take NQ = 0.5
W=J/s = N-m/s = kg-m^2/s^3
http://www.em.doe.gov/PDFS/Slurry%20Handling%20Workshop/2-Short%20Course%20Art%20Etchells/2-2%20DOEM4M5%20Slurry%20Handling%20Course_Part%202_Art%20Etchells_Dec31'07.pdf

## Slide 139
Blend time (estimation to within 5% desired concentration):
Notes: Q = discharge flowrate, or pumping capacity.
For “square-pitched” propellers in turbulent region, take NQ = 0.5
W=J/s = N-m/s = kg-m^2/s^3
http://www.em.doe.gov/PDFS/Slurry%20Handling%20Workshop/2-Short%20Course%20Art%20Etchells/2-2%20DOEM4M5%20Slurry%20Handling%20Course_Part%202_Art%20Etchells_Dec31'07.pdf

## Slide 140: Mixing Times of Miscible Liquids
Figure 3.4-6 shows a Correlation of mixing time for miscible liquid using a turbine in a baffled tank.
Mixing factor ft is defined as:
Where tT is the mixing time in seconds. For ,
ft is approximate constant, then tT N2/3 is constant.
For scaling up from vessel 1 to another vessel 2 with similar geometry and with same power/unit volume in the turbulent region, the mixing times are related by:

## Slide 142
The mixing time increases for the larger vessel.
For scaling up while keeping the same mixing time, the power/unit volume (P/V) increases markedly:
Usually, in scaling up to large-size vessels, a somewhat larger mixing time is used so that the power/unit volume does not increase markedly.

## Slide 143: Mixing Time
Notes: Batch mixing time
One measure of mixing performance is the batch mixing time. This has to convey some assessment of the asymptotic approach to homogenization, usually achieved in terms of the addition of a tracer and the subsequent approach to homogenization. The 95% mixing time is often used for this criterion.
The moment of tracer addition, is taken as zero, td is the dead time before the addition is first detected, tc the circulation time and tm the 95% mixing time, defined by the last measurement that lies outside the 5% band of the total concentration change.

## Slide 144
Example 3 Scale-up of Mixing Time in a Turbine Agitation System
Using the existing conditions for the turbine with a disk as in Example 1 part (a), do as follows:
Calculate the mixing time
Calculate the mixing time for a smaller vessel with a similar geometric ratio, where Dt is 0.30 m instead of 1.83 m. Do this for the same power per unit volume as used in part (a).
Using the same mixing time calculated for the smaller vessel in part (b), calculate the new power per unit volume for the larger vessel in part (a).

## Slide 145
Solution
In part (a), Dt = 1.83 m, Da = 0.61 m, Dt = H, N = 90/60 = 1.50 rev/s, ρ = 929 kg/m3, µ = 10 cp = 0.01 Pa.s. From example 1,
, Np = 5, P1 = 1.324 kW. For the tank volume,
The power per unit volume is
From the Figure 3.4-6 , , ft = 4.0. Substituting in Eq.

## Slide 146
For part (b)
* Mixing time decrease for smaller vessel from 17.30 to 5.73 s.

## Slide 147
For part (c)
tT2 = 5.73 s for smaller vessel
Calculate the P / V for the larger vessel

## Slide 153
Typical Dimensions for Mixing Equipment
G.B. Tatterson., Fluid Mixing and Gas Dispersion in Agitated Tanks, McGraw-Hill, 1991

## Slide 154
Typical Dimensions for Mixing Equipment
G.B. Tatterson., Fluid Mixing and Gas Dispersion in Agitated Tanks, McGraw-Hill, 1991

## Slide 155
Power Consumption and Scale-up in Mixing
Consider geometry, fluid properties, flow patterns, power, and so on. Has been considered through dimensional analysis.
Tatterson & Colson and Richardson.
With:
For geometrically similar vessels, ratios of all terms to right of the Froude number are negligible.
The Froude number is only important when significant vortex develops (in unbaffled tanks); for baffled tanks the NP does not depend on the Froude number.
Notes: P = power dissipation to the fluid. W=J/s = N-m/s = kg-m^2/s^3
Power rating of the driver must exceed P, i.e. has to overcome losses of driver, seals, bearing, etc.
As R.O.T., estimate losses as 25 % of calculated P
Therefore: Pdriver = 1.25 * P Use 1.75 factor when solids might settle on propeller before it is started.
(info from Cheremisinoff)

## Slide 156
Power Consumption and Scale-up in Mixing
Consider low viscosity, unbaffled systems.
Colson and Richardson.

## Slide 157
In-Class PS Exercise
Consider a solution of sodium hydroxide with the properties listed below. It is agitated by a propeller mixer that is 0.5m in diameter in a 2.28m diameter unbaffled tank. The liquid depth is 2.28m. The impeller is located 0.5m above the bottom of the tank. If the propeller is rotated at 2 Hz, what power is required?
Notes: Colson and Richardson

## Slide 158
Power Consumption and Scale-up in Mixing
Consider low viscosity, baffled systems.
Colson and Richardson.

## Slide 159
Power Consumption and Scale-up in Mixing
Consider low viscosity, baffled systems (wall baffles).
Colson and Richardson.
Figure 10.59 Power correlations for turbine impellers in a tank with 4 baffles. [w, D, impeller width and diameter, respectively.]
Notes: Curve 1 = Rushton impeller
Curves 2 & 4, open, flat blade impellers
Curve 5 is Backswept open impeller
Curve 6 is PBT (pitched blade turbine)

## Slide 160
In-Class PS Exercise
Assume you are mixing a small amount of material into water in a standard configuration baffled tank. The diameter of the pitched blade turbine is 1 m and it is desired to operate at 84 RPM. Estimate the power required.
Notes: http://www.em.doe.gov/PDFS/Slurry%20Handling%20Workshop/2-Short%20Course%20Art%20Etchells/2-2%20DOEM4M5%20Slurry%20Handling%20Course_Part%202_Art%20Etchells_Dec31'07.pdf

## Slide 161
Power Consumption and Scale-up in Mixing
Consider low viscosity, baffled systems (wall baffles).
N.P. Cheremisinoff, Handbook of Chemical Processing Equipment, B-H, 2000

## Slide 162
Power Consumption and Scale-up in Mixing
Propeller pitch:
Notes: Propeller pitch = (distance fluid (or propeller) travels in one full revolution) / (propeller diameter)

## Slide 163
Discharge Coefficient
N.P. Cheremisinoff, Handbook of Chemical Processing Equipment, B-H, 2000

## Slide 164
Mixing Time
P.M. Doran, Bioprocess Engineering Principles, 2nd Ed., Academic Press 2012
Blend time (estimation to within 10% desired concentration):
Notes: Ni tm = dimensionless mixing time or the number of stirrer rotations to mix the solution to homogenization.

## Slide 165
Mixing Time
P.M. Doran, Bioprocess Engineering Principles, 2nd Ed., Academic Press 2012
Doran suggests that for turbulent mixing conditions, irrespective of the impeller type, that (baffled vessel, single impeller, H=T):
Verified under aerated conditions also (impeller not flooded) and for:

## Slide 166
In-Class PS Exercise
A fermentation broth with properties as given below, is agitated in a 2.7 m3 baffled tank using a Rushton turbine with a diameter of 0.5 m and a stirred speed of 1 Hz. Estimate the mixing time.

## Slide 167
Additional Plots for Non-Standard Mixing
N.P. Cheremisinoff, Handbook of Chemical Processing Equipment, B-H, 2000

## Slide 168
Additional Plots for Non-Standard Mixing
N.P. Cheremisinoff, Handbook of Chemical Processing Equipment, B-H, 2000

## Slide 169
Additional Plots for Non-Standard Mixing
N.P. Cheremisinoff, Handbook of Chemical Processing Equipment, B-H, 2000

## Slide 170
Additional Plots for Non-Standard Mixing
N.P. Cheremisinoff, Handbook of Chemical Processing Equipment, B-H, 2000

## Slide 171: Heat Transfer in Agitated Vessel
Often it is necessary to cool or heat the contents of the vessel during agitation.
This is usually done by heat-transfer surfaces, which may be in the form of:
1) cooling or heating jackets in the wall of the vessel
2) coils of pipe immersed in the liquid.

## Slide 173
Vessel with heating jacket
When heating, the fluid entering is often steam, which condenses inside the jacket and leaves at the bottom.
The vessel is equipped with an agitator and in most cases also with baffles (not shown).
Correlations for the heat-transfer coefficient from the agitated Newtonian liquid inside the vessel to the jacket walls of the vessel have the following form:

## Slide 174
where:
h is the heat-transfer coefficient for the agitated liquid to the inner wall in W/m2.K,
Dt is the inside diameter of the tank in m,
k is thermal conductivity in W/m.K,
Da is diameter of agitator in m,
N is rotational speed in revolutions per sec,
ρ is fluid density in kg/m3,
µ is liquid viscosity in Pa.s

## Slide 177
EXAMPLE 4.13-1. Heat-Transfer Coefficient in Agitated Vessel with Jacket
A jacketed 1.83-m-diameter agitated vessel with baffles is being used to heat a liquid which is at 300 K. The agitator is 0.61 m in diameter and is a flat-blade turbine rotating at 100 rpm. Hot water is in the heating jacket. The wall surface temperature is constant at 355.4 K. The liquid has the following bulk physical properties: ρ = 961 kg/m3, cp = 2500 J/kg.K, k = 0.173 W/m.K, and µ = 1.00 Pa.s at 300 K and 0.084 Pa.s at 355.4 K. Calculate the heat-transfer coefficient to the wall of the jacket.

## Slide 180
Vessel with heating coil
Correlations for the heat-transfer coefficient to the outside surface of the coils in agitated vessel have the following form:
a) for a paddle agitator
b) for vertical baffle tube with a flat-blade turbine:
Do is outside diameter of the coil tube (in m), nb is number of vertical baffle tubes and µf is the viscosity of the mean film temperature

## Slide 183
Da1 | 5.00E-02 | m
J1 | 1.50E-02 | m
H1 | 1.50E-01 | m
DT1 | 1.50E-01 | m
E1 | 5.00E-02 | m
Da2 | 2.92E-01 | m
J2 | 8.77E-02 | m
H2 | 8.77E-01 | m
DT2 | 8.77E-01 | m
E2 | 2.92E-01 | m
Solution
1a

## Slide 184
N (rev/s) | P (J/s) | NRe | NP
4.00E-03 | 1.00E-09 | 1.00E+00 | 50
8.00E-03 | 5.12E-09 | 2.00E+00 | 32
2.00E-02 | 4.25E-08 | 5.00E+00 | 17
4.00E-02 | 1.60E-07 | 1.00E+01 | 8
4.00E-01 | 4.00E-05 | 1.00E+02 | 2
1.60E+00 | 1.28E-03 | 4.00E+02 | 1
4.00E+00 | 1.60E-02 | 1.00E+03 | 0.8
1.20E+01 | 2.70E-01 | 3.00E+03 | 0.5
6.00E+01 | 2.03E+01 | 1.50E+04 | 0.3
4.00E+02 | 4.00E+03 | 1.00E+05 | 0.2
4.00E+03 | 3.20E+06 | 1.00E+06 | 0.16
1b
From the graph

## Slide 186
1c
From the graph