## Slide 1: Construction Site Supervision
Prepared by Meseret Habtamu

## Slide 2: Table of content
General
The importance of supervision
The project environment
The skills and role of inspector
Defects in construction

## Slide 3: Chapter One: Introduction
Dictionary definition of inspection / supervision
  A critical examination of somebody or something aimed at forming a judgment or evaluation Microsoft® Encarta® 2009.
Construction Inspection/supervision: the process of ensuring targets(cost, time and quality) which has been set at the planning stage.
Inspection is one of the means of ensuring compliance of design and specifications.
The primary objective of inspection is to ensure safety of lives and durability of structure.
Therefore, the inspector has the responsibility of ensuring that the structure being built confirms to the acceptable standards and good workmanship and quality materials.
The inspector has professional as well as ethical responsibility to ensure that the structure is built correctly.

## Slide 4: …….Continued
Most of the buildings and other infrastructure fails due to lack of proper and professional supervision causing loss of lives and property.
Proper inspection becomes a critical aspect of a work in order to ensure that the works to be accomplished are done as intended, confirming to the technical documents requirement.
The relationship between the inspector and the contractor should be partnership rather than advisory and regulatory.

## Slide 5: ……Continued
It is common that inspectors takes side and may think that anything he/she can do to slow down, impede or control the work is to the advantage of the employer.
The inspector is responsible to control quality of work but if he/she impede the progress, the employer will incur additional costs.

## Slide 6: Importance of Supervision
Supervision is important to ensure that the structures or works being executed are constructed according to Design, Specification, code requirements as well as accepted practice.
Therefore, supervision can be defined as the process of ensuring compliance with technical requirements, government regulations and accepted levels of workmanship
If the work is executed with faulty supervision, it may result in
      change in the intention of the designer
      Unsafe and/ or unacceptable structure
      Additional costs to the employer
      Un necessary delay
      Poor quality of work, …etc

## Slide 7: The Project Environment
The influence of various elements in the executing inspector’s duties or the environment in which the inspector exercise his/her duties is called Project environment.
Factor affecting the project environment:
    Contractor attitude,
    Inspector attitude,
    Contractor abilities,
    Trade atmosphere,
    Field team ability,
    Completeness of drawings,
    Field conditions, …etc

## Slide 8: The Skills of Inspection
The inspector is excepted to have the following skills:
    Observation skills
        Global observation skills
        Abstract observational skills
    Technical skills or competence: Familiar with current technology and method of executing construction works
    Interpersonal skills: the way information is transmitted can affect the way it is understood.
    Communication skills: Exchange of information
      The sender is responsible for making the information clear, unambiguous, and complete so that the receiver can receive it correctly
        Written and oral, Listening and speaking
        Internal and external
        Formal and Informal
        Vertical and Horizontal

## Slide 9: Skill of inspection
    Communicating involves substantial body of knowledge that is not unique to the project context, for example
      Choice of media
      Writing style (Active vs Passive)
      Presentation technique
      Meeting management technique:
    Negotiating:
      Negotiation might be about the following things
        Scope, cost or schedule objective
        Contract terms and conditions
        Resource assignments, etc
    Problem solving skills
      Problem definition and decision making.
      Decision making, “ the right decision at the right time”
    Analytical skills : Analyzing the situation and weighing alternatives to arrive at a good decision.
      Looking at the big picture while at the same time separately understanding critical elements.

## Slide 10: The role of Inspector
An inspector may work for the Employer, the Contractor or the Consultant, in any case however, his responsibilities are the same.
Most of the time the inspector works on the side of the consultant.
The main role of supervisor in general is to follow up the execution of a project with the design, specification and appropriate legal and social practice.
The inspector must have a keen eye, be observant and able to see critically.

## Slide 11: The role of Inspector
  In most cases the inspector assumes role of advisory, however his/her main duties are limited to the following
    Inspect
    Guide
    Assist
    Facilitate
    Control quality but not to hinder work.
The controlling aspect of the inspection should only came in the event that the contractor fails to execute the works according to standards and accepted practice.

## Slide 12: …….Continued
The detailed knowledge of the plans and specifications for the particular work is very important for execution of his duties.
He/ she should be familiar with any revisions or amendments done to the original documents and also the reason for such changes and their incorporation to the works.
He/she must also be able to follow the progress of the work, record accurately and follow up the day-to-day progress.
He/ she must record and advice rectifications of errors observed during inspection of works.

## Slide 13: …….Continued
The inspector needs to exercise professional integrity and high ethical standards.
The inspector shall not stop the work unless otherwise it will leads to death.
He/ she must always understand the problem of the contactor and find a solution to assist him in resolving the issues without waiving any of the specific requirements of the specification.
In summary the inspector must have the following,
    Knowledge
    Integrity
    Ability
    Good judgment
    Good attitude
    practice

## Slide 14: …..Continued
His/her specific duties are summarized below:
    Ensuring compliance by the contractor with drawings, specifications and contractual provision of the project.
    Monitoring project progress according to the schedule
    Coordinating and monitoring different tests
    Inspecting contract drawings and specifications
    Rejection of works which is not within the contractual quality
    Stopping of works when safety concern override basic contractual commitment.
    Approval or rejection of shop drawings, materials and samples
In other hand the inspector has no authority to revoke, alter, enlarge, relax, or release any of the requirements of the contract provisions.

## Slide 15: Necessary Equipments
Make sure that you have the following equipments at hand whenever inspecting a site
    Tape mater
    Level
    Straight edge
    Note book, diary
    Safety helmet
    Suitable site shoes
    Appropriate clothing

## Slide 16: Defects in Construction
Defects in construction may appear due to either of the following reasons
    Inadequate strength or stiffness
    Structural instability
    Settling of foundations
    Distressed structural members as evidenced by cracking, movement and excessive deflection
    Weather and moisture intrusion caused by failure of roofing, exterior wall, floors and openings
    Premature depreciation such as abnormal wear, decay, corrosion
    Poor Workmanship
    Un-adequate Supervision
    Usage of poor quality material
Some of this defects will result in buildings or parts of buildings that are unsuitable or unusable. Others will result in excessive operating and maintenance costs, premature replacement costs, or depreciated or unacceptable appearance and sometimes property damage, personal injury or death.

## Slide 17: ……… Continued
Defects in structure can occur during the construction period or during times of use.
The inspector is required to analyze the situation and arrive at a technically sound explanation as well as possible practical recommendations.
The inspector is therefore expected to answer the following key questions for analyzing the defect and forward the possible recommendations
    What is the phenomenon?
    How can it be described and explained?
    What is the exact cause?
    How it can be rectified?
      By removal or replacement?
      By repair?

## Slide 18: … Continued
    By coating?
    By strengthening?
    By premature replacement?
    By acceptance of defects and monetary adjustments?
    By some equivalent to the originally specified product or procedure?
    By some creative or innovative procedure?
The inspector should also understand the costs of remedial measures.
    Costs of analysis and recommendation.
    Costs of Redesign works
    Costs of inspection and testing
    Costs of labor, material, equipment coordination
    Costs of consequential damages
    Costs due to loss of use of building
    Costs due to damage of personal injuries.

## Slide 19: Identifying the source of responsibilities
Who is responsible for the failure
  Design problem?
    Was the construction project properly design?
      The architect and the engineers are primarily responsible for the design problems. Who is responsible for Temporarily structures?
  Construction problem?
    Was the project built in accordance with contract requirement? Was it properly constructed? Does the contractor provide right materials as per the specifications.
      Who is responsible?
  Maintenance or usage problem?
    Was the project and all its systems been properly cared for? Has the project been abused or damaged by its user? has the project been used improperly?
      Who is responsible?
  Unforeseen circumstance [natural disaster, war, …etc]
      Who is responsible?
  Faulty supervision
      Who is reponsible?
Accidents are very common in construction sites, hence, it is very important that healthy and safety issues are addressed properly.

## Slide 20: … Continued
Commonly accidents occur due to the following reasons
      In-adequately installment of formworks
      Improper construction of temporary structures
      Improper nails
      Un-braced underground excavations
      Improper usage of equipments
      Negligence of the workers
      Un usage of safety equipments