## Slide 1: Specification & Quantity Survey
By
Eshetu TS.

## Slide 2: Chapter 4 Cost Estimation
4.1 Project Cost Estimation
Project Cost estimation is the process of valuing on monetary expression, including the cost of all possible entrants necessary for the planning, implementing and monitoring stages of the proposed project under consideration.
The possible entrants are:
- Preliminary investigation (project appraisal costs)
- design and supervision (consultancy cost )
- construction works (contractor’s cost )
- land owning cost, and
- monitoring costs

## Slide 3
4.2 Purpose of Cost Estimation
The main purpose of costing or estimating are to:
• know the volume of work in reference to the fund available
• determine actual cost per unit of item
• Identifying engineering estimate of the work for bidding purpose
• work out economical use of materials , labor and equipments
• In cases of variations to determine the extra cost to be incurred
• when changes in cost due to legislation happens, to work out the escalation in cost

## Slide 4
The following information is required to define cost per unit of work
1. Correct information of the market price of the materials at the time of need to be used as a basic price.
2. Correct information of the rates of various categories of skilled and unskilled laborers as wage rates to be used for daily work rate.
3. Output of laborers per day for various types of items (productivity)
4. Correct information of the rates of various categories of equipments and tools as rental rates to be used for major items of rates.
5. Up-to-date knowledge of the construction methods.

## Slide 5
4.3 Factors affecting cost estimation
1) Type and documentation of the project
2) Construction scheduling
3) Bidding environment
4) Quality and availability of material and labor
5) Construction facilities /tools and method of construction
6) Location of the site: Transportation charges
7) Proper management
8) Land charges (lease)
9) Nature of subsurface condition

## Slide 6
Types of Costing or Estimation
I. Preliminary /approximate costing
Rates are determined either from practical knowledge or from records of similar previous works.
This type of cost estimation is required to know the financial position of the client before costly detailed designs are carried out.
Examples of approximate cost estimations are as follows:

## Slide 7
A. Cost per functional unit
Hospital =cost per bed,
Dormitory = cost per student,
Cinema or theatre = cost per seat,
residential buildings = cost per area,
road works = cost per kilometer length,
culverts or bridges = cost per meter span,
water supply or sewerage projects = cost per head of population.

## Slide 8
B. Plinth area method – cost per m2
This estimate is prepared on the basis of plinth area of the building.
The rate per meter square is deduced from the cost of similar building projects in the locality.
The plinth area shall be calculated based on the roof area, by taking external dimensions of the building at the plinth level.

## Slide 9
C. Cubical Content method – cost per m3
The estimate is based on cubical contents of various buildings, i.e. plinth area of the building x height x cubic content rate.
Height should be taken from the top of flat roof (or halfway of the sloped roof) to the top of concrete in foundation.

## Slide 10
Purpose of approximate Estimate
i) To investigate feasibility
ii) To save time and money
iii) To investigate benefit and comparison of cost with utility.
iv) Adjustment of Planning.
v) To obtain administrative approval:

## Slide 11
II. Detailed cost estimate( based on item rate)
This is the most reliable and accurate type of estimate.
The quantities of items are carefully prepared from the drawings and the total cost worked out from up to date market rates.
A detail cost estimate thus requires quantity surveying and analysis of the different rates for the quantities prepared.

## Slide 12
Composition of Project Price
The total price of a construction project is the sum of direct costs, contingency costs, and margin.
Direct costs: are the labor, material, and equipment costs of project construction.
Contingency costs: are those that should be added to the costs initially calculated to take into account events, that are likely to occur during the course of the project and affect overall project cost.
Margin (sometimes called markup): has three components: indirect (distributable) costs; company-wide (general & administrative) costs; and profit.

## Slide 13
Indirect costs: are project-specific costs that are not associated with a specific physical item. They include the cost of project management, payroll preparation.
Company-wide costs include:
(1) Costs that are incurred during the course of a project but are not project related.
(2) Costs that are incurred before or after a project.
Profit: is the amount of money that remains from the funds collected from the client after all costs have been paid.

## Slide 14
Disposition of the Cost Calculation
Direct itemized costs:
A. Material costs
    Construction/Building material
    Operating supplies
    Loading, unloading and transportation costs
    Wastages

## Slide 15
required information:
  Quantity of material required to produce a unit amount of itemized work
  Basic price (Prime cost) at the source of material
  Transport, loading and unloading to the site
  Waste/loss (e.g. Breaking, rupture, defective material, wastage etc).

## Slide 16
B. Labor costs: include
Standard wages
Extra and supplementary pay for
  Production bonus
  Long continuity of Service (permanent laborer)
  Over time pay
  Property creating performance
  Less favorable condition

## Slide 17
Social Service payments
    Holiday pay if any
    Health insurance
    Unemployment insurance
    Payment during sickness

## Slide 18
Required information for the calculation of labor cost
Number and type of skilled and unskilled manpower for a particular type of work, (Crew)
Performance of crew per hour for a unit amount of work
Indexed hourly cost of the workman ship.
Utilization factor of the workmanship. Share of a particular personal per hour for the specified work.

## Slide 19
C. Equipment costs: - All costs for commissioning /holding and operation of the equipment.
          ownership of plant
          hire of plant
- Standing Costs: includes capital sum based on purchase price and operating cost, maintenance, tax and insurance.
Operating Costs: operators cost, fuel, consumable stores.
Required information:
Type of equipment for a particular item of work.
Performance of equipment per hour for a unit amount of work (production rate)

## Slide 20
D. Costs for sub-contractor:- If the work is to be Sublette to a nominated subcontractor, the cost shall be determined and separately established as a sub contractor fee.
Ex. –Marble cladding
-Supply and fix items (aluminum frames)
-Furniture etc.

## Slide 21
ii) Indirect Costs
A. Site over head costs
            Time-independent costs
Costs for site plant/ site installation
Cost for site facilities
Engineering and controlling
Operation risks
Special costs

## Slide 22
          Time-dependent costs
Commissioning /holding costs
Operating costs
Costs for contractor’s agent
B. General overhead costs
C. Risks and profit

## Slide 23
Direct cost + Site overhead Cost = Production cost
Production cost +General overhead cost = Self-costs
Self- costs + Risk& profit = Bid sum
Bid sum + Vat = Bid sum inclusive vat.

## Slide 24
Example
a) Calculation of material cost
1) Calculation of the material costs of 1m3 concrete C-25 grade given.
-1Qtl of cement -355 Birr
-1truck of Sand (6 m3 ) from source to Site 1500 Birr
-1 truck of gravel (6m3) from source to site 1200 Birr
-1m3 water 10 Birr
-Transportation cost 5 Birr/Qtl/Km
-Wastage 5%

## Slide 25
Type of material | Unit | Qty | Unit rate | Cost/unit
Cement | Qtl | 7 | 355 | 2485
Sand | M3 | 0.5 | 250 | 125
Gravel | M3 | 0.75 | 200 | 150
Water | M3 | 0.3 | 10 | 3
Sum |  |  |  | 2763
Loss 5% 138.15
Total 2901.15 Birr/m3

## Slide 26
Labour | No | UF | Index hourly cost | Hourly cost (Birr)
Forman | 1 | 1/2 | 10 | 5
mason | 1 | 1 | 7.5 | 7.5
engineer/manager | 1 | 1/10 | 56.8 | 5.68
Assistance mason | 2 | 1 | 5.5 | 11
D. Laborer | 18 | 1 | 4 | 72
Total |  |  |  | 101.18
b) Calculation of Labor cost
Calculation of labor cost for a m3 of concrete; production rate 1.25 m3 /hr
Labour cost = 101.18/1.25 = 80.944/m3

## Slide 27
C) Calculation of Equipment cost
Calculation of equipment cost for m3 of concrete
Mixer - Original cost = 500,000 Birr
Useful life = 3yrs
Monthly repair cost with supplies: - 700 Birr
Vibrator- Original cost = 350,000 Birr
Useful life = 7yrs
Repair cost monthly = 450 Birr
Assume 8 working hours per day and 22 days per month

## Slide 28
Two methods of calculation are followed.
I) With charges accounted for depreciation, interest return and monthly repair costs
II) With monthly rental charges.
Hourly equipment cost
i) Mixer
Depreciation (d) =500,000 Birr = 78.9 Birr/hr
3x12(22x8) hr
Hourly repair cost = 700/8x22 = 3.98 Birr/hr
Hourly Mixer cost = 78.9 + 3.98 = 82.88 Birr/hr

## Slide 29
ii) Vibrator
Depreciation (d) = 350,000/(7x12x8x22) =23.6Birr/hr
Repair cost = 450/(8x22) = 2.5 Birr /hr
Hourly vibrator cost = 23.6+ 2.5 = 26.1 Birr/hr
Total hourly cost (Birr) = 108.98 Birr/hr
Equipment cost for (1m3 concrete) 108.98/1.25 = 87.18 Birr/ m3

## Slide 30
Equipment cost using monthly rental changes
    Mixer= 500,000 Birr Month rental charge
    Vibrator = 350000 Birr month rental charge
Hourly cost
  Mixer 500000/22x8 = 2841 Birr/hr
  Vibrator = 350000/22x8 = 1988 Birr /hr
Total = 4824Birr/hr
equipment cost for 1 m3 of concrete = 4824/1.25
= 3863.2Birr/ m3

## Slide 31
Two approaches for cost calculation
i/ Cost Calculation with predetermined charges
Example: Establish the unit price of 1 m3 concrete considered for in the previous examples.
Given that the surcharge for the indirect cost is 35%.
    Material cost= 1633.8
    Labor cost = 74.88
    Equipment cost = 87.18
Direct cost = 1795.86
Indirect cost = 0.35 (1795.86) = 628.55
Unite price = 1795.86 + 628.55 = 2424.41 Birr/ m3

## Slide 32
ii/ Cost calculation through the bid Sum
In this approach, amounts for site overhead costs, general overhead costs, risk and profit are to be ascertained separately for each project.
Here from surcharges on direct itemized costs result with different amount for each project;
Four steps for this calculation method:
- Establishing the production costs
- Establishing the bid sum
- Establishing the surcharges on direct itemized costs
- Establishing the unit prices

## Slide 33
Given the following detail for the construction of 5Om long fence around a site.
1/ List of items quantities and direct itemized costs are as given in the table.
No | work | Unit | Qnt | Direct cost
1 | Excavation to a depth of 1m | M3 | 40 | 20
2 | 50 cm thick masonry wall | M3 | 25 | 50
3 | Concrete for tie beam | M3 | 5 | 50
4 | Dia 14 dc formed ban | Kg | 245 | 8.5
5 | Dia 8 stirrups | Kg | 132 | 4.5
6 | Formwork tie beam | M2 | 20 | 70
7 | 20cm thick HCB wall | m2 | 90 | 50
 | Direct cost |  |  | 703,000

## Slide 34
2) Site overhead costs
Site facilities (office, store---) -------------------2500 birr
Electricity, water & telephone --------------------800 birr
Salary professionals -----------------------------2000 birr
Secretarial service ---------------------------300 birr
3) General overhead cost ----------------10 % production cost
4) Risk & profit ---------------------------7% of production cost

## Slide 35
Question: Establish bid sum and unit prices for the itemized works.
Step 1: Establish production cost. (Direct cost + Site overhead cost)
        Direct cost :- 703,000 birr
        Site overhead cost :- 5,600 birr
        Production cost 708,600 birr
Step 2: Establish bid sum [production cost + General overhead cost + risk & profit]
Production cost -------------------------- 708,600 birr
General overhead cost = 10%(708,600)=70860 birr
Risk & profit ---------------7 %(708,600)= 49602 birr
Bid sum without vat = 829062 birr
vat 15% = 124321.3
Bid sum with vat = 953421.3 birr

## Slide 36
Step 3: Surcharge on direct itemized cost
Surcharge = Bid sum without vat
Direct itemized cost
= 829062/ 703,000 = 1.2
Step 4: Establishing unit prices
Unit price = Surcharge x direct itemized cost

## Slide 37
No | work | Unit | Qnt | Unit price | amount
1 | Excavation to a depth of 1m | M3 | 40 | 24 | 960
2 | 50 cm thick masonry wall | M3 | 25 | 60 | 1500
3 | Concrete for tie beam | M3 | 5 | 60 | 3000
4 | Dia 14 dc formed ban | Kg | 245 | 10.2 | 1479
5 | Dia 8 stirrups | Kg | 132 | 5.4 | 712.8
6 | Formwork tie beam | M2 | 20 | 84 | 1680
7 | 20cm thick HCB wall | m2 | 90 | 60 | 5400
Bid sum without vat 14731.8
Add 15 % vat 2209.77
Bid sum with vat 16941.57birr

## Slide 38
VALUE ENGINEERING
Value Engineering is a systematic and organized effort to identify the functions of a product, system or procedure and to attain that function with minimum cost without jeopardizing quality, aesthetics, appearance etc.
Value engineering studies may be performed by Consultants during design development, or by the contractor during construction.
The most effective time to conduct such studies is during design development.

## Slide 39
The value of a component or system can be defined as its function plus quality divided by its lifecycle cost.
Value of a component = ( Function + Quality )
Life Cycle-Cost
Life-Cycle Cost = Initial or Construction Cost + Operating Cost+ Maintenance Cost+ Depreciation Cost – any Salvage Value.
Value Engineering seeks the highest value design components by Improving utility with same cost or maintains same function with less cost.

## Slide 40
In general Value engineering:
Enhances value of money,
Effects improvements in function, performance and quality,
Enables people pin point areas that need attention and improvement,
Provides a method of generating ideas and alternatives for possible solution to a problem,
Provides a vehicle for dialogue,
Documents the rationale for decisions,
Improves the value of goods and services.

## Slide 41
Steps in Value Engineering
1) Information Gathering:
The information gathering phase involves studying the design to identify potential components or systems for detailed study.
2) Speculation through Creative Thinking:
The purpose of the speculation or creative phase is to identify alternative ways to accomplish the essential functions of the items selected for the study.
The intent is to develop a list of alternative materials or components that might be used.

## Slide 42
3) Evaluation through preliminary Life-Cycle Costing:
The evaluation phase involves determining the most promising alternatives from the set identified in the speculation phase.
The intent is to determine which alternatives will meet the owner’s functional requirements and provide more value to the completed project.
4) Development of Technical Solutions:
The development phase involves creating design concepts for the alternatives identified during the evaluation phase.
Alternatives are compared, and the ones representing the best value are selected for presentation to the designer and the owner.

## Slide 43
5) Presentation of Alternative Options:
The final step is the preparation of the value engineering proposals, in which detailed technical and cost data are developed to support the recommendations.
The proposals are submitted to the designer and the owner for approval.
If approved, the proposals are incorporated into the design. If not approved, the design is not changed